27.10.2006

EEA INFORMATION PROCEDURE ON DRAFT TECHNICAL REGULATIONS ACCORDING TO

DIRECTIVE 98/34/EEC (ANNEX II, CHAPTER XIX, 1. EEA AGREEMENT)

TO:	ESA

1.

2.	N

3.A.	ROYAL MINISTRY OF TRADE AND INDUSTRY,

Economic Policy Department

P.O. BOX 8014 Dep

N-0030  OSLO

3.B.	Norwegian Maritime Directorate
	Offshore Department

P.O. Box 2222

NO-5509 HAUGESUND

Tel: +47 52745000

4.	2006/9020/N

5.	In Norwegian: Utkast til forskrift om evakuerings- og redningsredskaper på flyttbare innretninger

In English: Draft regulation concerning evacuation and life-saving appliances on mobile offshore units

6.	Life saving and evacuation appliances on board Mobile Offshore Units (MOU’s).

7.

8.	The draft regulation applies to Norwegian flagged Mobile Offshore Units.

The draft implies that the most recently adopted requirements in force will apply to all MOU’s, irrespectively of age. Previous approved MOU’s will have to make necessary upgrades as a result of this new regulation.

The definition of “company” is suggested to be harmonised with the definition given in the Ship Safety Act, § 4.

The draft regulation contains provisions which regulate the requirements for life-saving appliances. The suggested changes to these requirements are:

- § 8 (1) litra f and g, concerning general requirements for life-saving appliances. New requirements on documentation on design of free-fall lifeboats and stowage of such lifeboats have been added.

- § 10, concerning radio appliances. The draft updates and clarifies the requirements for radio equipment on board the lifeboats and rescue boat so that they harmonise with IMO resolution A.809(19).

- § 11 (1) litra a, concerning launching arrangements and that they are to be securely stowed. Other changes to § 11 are adjustments of requirements from the regulation of 2003. These have been moved to clarify which type of lifeboats they are applicable to.

- 12 litra a, concerning testing of life-saving appliances. The draft contains new requirements regarding documentation of acceptance criteria to ensure that the lifeboats can handle the environment they are designed for. In § 12 litra d, a requirement concerning testing of free-fall lifeboats every fifth year has been added.

- 22 (5), concerning drills. Additional requirement regarding free-fall lifeboats and an annually simulated launch had been added.

Other new provisions in the draft regulation are:

- § 9 (4), concerning immersion suits. The draft introduces a new test procedure for immersion suits and clarifies the requirements stated in the regulation of 2003.

- § 20, concerning the marking of evacuation routes.

§ 21, concerning the on board safety plan.

9.	Regulations no. 492 of 11 April 2003 concerning life-saving appliances and evacuation on mobile offshore units, which will be repealed five years after the new regulations enters into force.

11.	No

12.

13.	No

14.	No

15.	a) Information on the impact assessment can be found on page 13.

16.	TBT Aspects

b) i

SPS Aspects

b) i