26.01.2007

EEA INFORMATION PROCEDURE ON DRAFT TECHNICAL REGULATIONS ACCORDING TO DIRECTIVE 98/34/EEC (ANNEX II, CHAPTER XIX, 1. EEA AGREEMENT)

TO:	ESA

1.

2.	N

3.A.	ROYAL MINISTRY OF TRADE AND INDUSTRY,

Economic Policy Department

P.O. BOX 8014 Dep

N-0030  OSLO

3.B.	Norwegian Post and Telecommunications Authority
P.O. Box 447, Sentrum
N-0104 OSLO
Norway

4.	2007/9003/N

5.	Proposed amendment for regulation on safety in electronic communications networks

6.	Cabel TV networks and equipment being an integral part of cabel TV networks. Retailers of TV sets are required to supply insulated connections cf. article 8.

7.

8.	The regulations lay down electrical insulation requirements on the connection between the electronic communications networks coaxial wall socket and the connected terminal equipment. This connection is defined as a part of the electronic communications network. All new and rebuilt electronic communications networks of such kind shall be fitted with such electrical insulation. Retailers of TV sets are required to supply insulated connections.

9.	The main objective is to prevent risk of fire wenn connecting modern LCD and plasma TV sets to electronic communications networks with a coaxial wall socket. Several such TV sets have taken fire or set fire to networks. It happens because in the terminal equipment there is a galvanic connection between the AC power line earth and the equipment sockets used for connection to the electronic communications networks.

10.	Regulation on safety in electronic communications networks

11.	NO

12.

13.	No

14.	No

15.

16.	TBT: a) NO b) iii)

SPS: a) NO b) iii)