Regulation draft – amendment in regulation on measuring systems for the continuous of quantities of liquids (other than water).

# I

The following changes are made in annex 2 in regulation of 26. april 2006 nr. 466 on measuring systems for continuous measurements of quantities of liquids (other than water):

Table 5 in point 7 concerning "specific requirements" should be:

7.	Putting into use - requirements on accuracy class for measuring instruments

| Table 5 |
| --- |
| Accuracy class | Types of Measuring system |
| 0,3 | – Measuring systems on pipeline – Measuring systems when used for the levying of taxes and duties on mineral oils when loading and unloading ships, and rail and road tankers. |
| 0,5 | All measuring systems if not differently stated elsewhere in this Table, in particular: – fuel dispensers (not for liquefied gases), – measuring systems on road tankers for liquids of low viscosity (< 20 mPa.s) – measuring systems for loading/unloading ships and rail and road tankers – measuring systems for milk – measuring systems for refuelling aircraft |
| 1,0 | Measuring systems for liquefied gases under pressure measured at a temperature equal to or above -10 °C Measuring systems normally in class 0,3 or 0,5, but used for liquids – whose temperature is less than - 10 °C or greater than 50 °C – whose dynamic viscosity is higher than 1 000 mPa.s – whose maximum flowrate is not higher than 20 L/h |
| 1,5 | Measuring instruments for liquefied carbon dioxide Measuring systems for liquefied gases under pressure measured at a temperature below – 10 °C (other than cryogenic liquids) |
| 2,5 | Measuring systems for cryogenic liquids (temperature below – 153 °C) |
| Note: However, the manufacturer may specify a better accuracy class for a certain type of measuring system. |

# II

The amendment shall immediatly enter into force.