Regulations on Metrological Control

of Measuring Systems for Fuel Dispensers, Road Tankers and Milk

CHAPTER I

Scope and Definitions

Art. 1

Scope

The present Regulations apply to measuring systems for fuel dispensers, road tankers and milk intended for continuous and dynamic measurements of volume when used for direct sales to the public and for  commercial transactions.  Measuring systems to which the present Regulations apply shall meet the requirements and be subject to the metrological control stipulated in the present Regulations and the rules referred to therein.

There may be placed on the market and put into use according to para. 1, EEC-measuring systems and MID-measuring systems.

Art. 2

Definitions

The following definitions shall be used concerning measuring systems, cf. Para. 1, Art. 1:-

- EA (European Co-operation for Accreditation) is an European association for accreditation, cf. Act No. 24/2006 on Accreditation et al.

- EEC verification is undertaken by the Consumer Agency or another legal authority in the EEA in conformity with rules in an EEC Directive.  An inspection is undertaken in order to acquire data to the effect that a measuring instrument is in conformity with EEC type approval thus meeting requirements, markings affixed on the instrument and a certificate is issued.

- An EEC type approval is implemented by a legal authority in the EEA in conformity with the rules of an EEC Directive and denotes a determination granting approval of the fact that the construction of a measuring instrument satisfies the defined requirements.  Type approval is based on a thorough test of type and is a prerequisite of an EEC verification.

- EEC measuring systems are measuring systems which are manufactured in conformity with Directive 77/313/EEC on measuring systems for liquids other than water and which have a valid EEC type approval issued before 30 October 2006, carry correct marking relating thereto and are sealed, cf. Regulations No. 129/1994 on Measuring Instruments and Methods of Metrological Control.  EEC-measuring systems shall have EEC-verification prior to being put into first use.

- The owner of a measuring system is an individual, a legal person or a guarantor who is responsible for a measuring system coming under the scope of the present Regulations.

- A fuel dispenser is a measuring system intended for the refuelling of motor vehicles, small boats and small aircraft.

- Internal control is in the present Regulations used in the meaning contained in para. 2, Art. 14 of Act No. 91/2006 on Measurements, Measurement Standards and Official Weighers and according to further provisions in the present Regulations.

- Reverification is an act to ensure and confirm formally that a measuring instrument meets all requirements of Laws and Regulations.  Reverification is performed by inspection, marking and/or the issue of a certificate and is usually completed by sealing of access to settings.

- MID measuring systems are measuring systems which do not have valid EEC type approval before 30 October 2006 and which come under the provision in Annex MI-005, cf. Regulations No. 465/2007 on the implementation of the Directive of the European Parliament and the Council No. 2004/22/EC on Measuring Instruments and meet the applicable requirements, carry correct markings thereon and are sealed.  The conformity assessment of MID-measuring systems shall be completed prior to these being put into first use.

- A measuring system is a system that comprises the meter itself and all devices required to ensure correct measurement or intended to facilitate the measuring operations.  Measuring systems are divided according to Table 5 in Directive 2004/22/EC as per use into measuring system on pipeline, measuring system for liquified gases, measuring system for cryogenic liquids and other measuring systems which are specifically for fuel dispensers, road tankers, loading and unloading of ships and road tankers, milk and finally for refuelling aircraft.

- A meter is an instrument designed to measure continuously, store and display the quantity  at metering conditions of liquid flowing through the  measurement transducer in a closed, fully charged conduit.

- Measuring instruments supplier is a manufacturer, an authorized representative, a vendor or a distributor of measuring systems coming under para. 1, Art. 1, cf. Art 8 of Act No. 91/2006.

In addition to the aforementioned definitions there shall be used the definitions listed in Art. 4 of Directive 2004/22/EEC on Measuring Instruments and which are in Annex MI-005 thereto for MID-measuring systems.

CHAPTER II

Types of Meters, Marking and Accuracy Classes.

Art. 3

Permitted Types of New Measuring Systems

It is not permissible to place on the market new measuring instruments and put these into use cf. para. 1, Art. 1, other than EEC- or MID-measuring systems.

An EEC-measuring system shall be marked in conformity with the EEC type approval prior to being placed on the market and shall have EEC verification prior to it being put into first use, cf. Regulations No. 129/1994 on Measuring Instruments and Methods of Metrological Control.

Proof to the effect that requirements for EEC-measuring systems are being met shall be available in certificates on EEC type approval and EEC verification and with markings in conformity with provisions in Regulations No. 129/1994 on Measuring Instruments and Methods for Metrological Control.

MID-measuring systems shall meet the pertaining requirements concerning conformity in Directive 2004/22/EC on Measuring Instruments, including conformity with the essential requirements made in Annex I and the specific requirements made in Annex MI-005 to the Directive prior to these being placed on the market and put into first use.

Proof to the effect that conformity requirements of MID-measuring systems be met shall be at hand in writing in a declaration of conformity which has been made in a manner which is stipulated in Art. 9 of Directive 2004/22/EC on Measuring Instruments with CE-marking and the supplementary metrology marking in conformity with the provisions Art. 7 and 17 of the Directive.

Art. 4

Continued use of Older Types of Meters

For tasks under para. 1, Art. 1 there may be used measuring systems other than EEC- and MID-measuring systems which have already been taken into use while these measure correctly, cf. the provisions of Chapter V.

Art. 5

First Use and Marking

EEC-measuring systems shall obtain reverification prior to being put into first use.

MID-measuring systems are considered to have reverification for first use, cf. Art. 14 in case conformity assessment has been fully completed and installation meets the requirements of Art. 7, provided these carry special marking for new measuring systems, cf. Regulations No. 955/2006 on Reverification Symbols and Markings of Measuring Instruments Subject to Control.

Art. 6

Temperature and Accuracy Classes

Measuring systems for fuel dispensers shall show the delivered volume at metering conditions in commercial transactions and direct sales to the public without the use of conversion device taking account of temperature.

The requirements, stipulated in clause 7 to Annex MI-005 in Directive 2004/22/EC on Measuring Instruments and stating that specific accuracy classes shall be used, subject to for which purpose the MID-measuring system is used, are minimum requirements.

CHAPTER III

On Responsibility of Parties

Art. 7

Requirements for Suppliers

A measuring instrument supplier may not market, sell or deliver water meters for use according to para. 1, Art. 1 unless these meet the provisions of Art. 3 and other pertaining provisions in the present Regulations.

When a manufacturer himself undertakes installation of MID-measuring systems it is permissible to take a measuring system into use without prior reverification and the same applies to distributors undertaking installation with the approval and in accordance with the manufacturer’s instructions in case the distributor has submitted stipulated documents and been registered with the Consumer Agency.

Art. 8

Requirements for Owners of Measuring Systems

An owner of a measuring system is responsible for obtaining reverification from a Testing Laboratory commissioned for that purpose, cf. Regulations 956/2006 on the Mode of Work of Those Undertaking the Reverification of Measuring Instruments as commissioned by the Consumer Agency.

An owner of measuring systems may not instal or have these installed for use according to para. 1, Art. 1 unless these meet the provisions og Art. 3 and other pertaining provisions in the present Regulations.

An owner shall abide by a manufacturer’s conditions concerning the use and permitted operating conditions.  For MID-measuring systems regard shall be had for requirements in clause 1.3 in Annex I and clause 1 in Annex MI-005 in Directive 2004/22/EEC on Measuring Instruments.

It is the responsibility of the owner of a measuring system to see to it that errors in use do not exceed the double error limits applied as a reference for new measuring systems, cf. Chapter V.

Art. 9

Requirements for Service Parties

A measuring system which is used in accordance with para. 1, Art. 1 and has a broken seal, has undergone repair so that this may influence its accuracy or has been moved shall be submitted to reverification prior to its being taken into use again, see, however, service party permission in Art. 14.

A service party who has performed any act requiring reverification, cf. para. 1, shall forthwith notify the owner thereof.

CHAPTER IV

EEC-Verification and Conformity Assessment of MID-Measuring Systems

Art. 10

EEC Verification of EEC-measuring systems

A manufacturer is responsible for acquiring EEC verification with legal authorities of Member States of the EEA Agreement or those undertaking verifications as commissioned by them.

The Consumer Agency may commission a testing laboratory to undertake EEC verification if it has accreditation for the pertaining tests and inspection.

Art. 11

Conformity Assessment of MID Measuring Systems

A manufacturer is responsible for a conformity assessment of a MID measuring system.  He undertakes this himself with the participation of notified parties in accordance with instructions of the conformity assessments modules described in Annexes A, B, D, F, G and H1 to Directive 2004/22/EEC on Measuring Instruments, cf. also Regulations No. 957/2006 on Modules for the various stages of the conformity assessment and rules on affixing and the use of CE-conformity marking intended for use in Directives on Technical Harmonization.

In case a supplier or service party undertake some part of the conformity assessment which a manufacturer is permitted to do, it is the responsibility of the manufacturer and the party concerned to meet the selfsame requirements as are addressed to the manufacturer on account of the conformity assessment.

CHAPTER V

Reverification and Testing of Measuring Systems in Use

Art. 12

Reverifications

Reverifications of measuring systems are total inspections, i.e. each individual meter is reverified upon the end of the term of validity.

Reverifications are undertaken by a party dealing with the reverification of measuring instruments commissioned by the Consumer Agency, cf. Regulations No. 956/2006 on the Mode of Work of Those Undertaking the Reverification of Measuring Instruments as commissioned by the Consumer Agency, see, however, Art. 15 on internal control replacing reverifications.

Reverified measuring system shall be marked by means of a reverification symbol, cf. Regulations No. 955/2006 on Reverification Symbols and the Markings of Measuring Instruments Subject to Control.

Art. 13

Reverification Testing

In order that measuring systems pass testing deviations may not exceed the maximum permissible errors .  This applies to each item being tested as applicable.  A measuring system shall be sealed if it has parts which may not be removed or adjusted prior to a reverification symbol being affixed.

There shall be a test of typical flow and for the volume which the testing parties´ volumetric tanks permit with the reservation that small volumetric tanks can cause to large uncertainty for the test.  Test shall be undertaken at a minimum at Qmax-real for a typical sales volume such as 20 or 25 litres in the case of sales pumps for fuel.  In the instances when water is used upon testing of milk meters the maximum permissible errors are in the range of 0% - 1,0%.

Upon reverification care shall be taken that the type, marking and accuracy class of a measuring system be in conformity with the liquid being measured.

EEC-measuring systems shall upon reverification meet requirements for markings in conformity with provisions of Regulations 129/1994 on Measuring Instruments and Methods of Metrological Control and in conformity with requirements concerning environment and application.  Upon testing errors shall be within the limits which are comparable to requirements in clause 2 in Annex MI-005 in Directive 2004/22/EC on Measuring Instruments.

MID-measuring systems shall upon reverification meet requirements of Annex MI-005 in Directive 2004/22/EC on Measuring Instruments for environment and application in conformity with the values specified by the manufacturer concerning permitted operating conditions and errors shall be within the limits given in clause 2 of Annex MI-005 for the maximum permissible errors.  Testing of MID measuring systems shall be performed at the same or similar volume and flow as applies to EEC-measuring systems.

Measuring systems older than EEC- or MID-measuring systems shall meet the selfsame requirements as EEC-measuring systems concerning environment, application and errors, but it is permissible to reverify older measuring systems which have previously been reverified although markings be not in complete conformity with requirements, provided that minimum markings are shown.  Minimum markings are the manufacturer, type, maximum flow, minimum flow, permitted minimum sales volume and serial No.

Art. 14

Reverification periods and Approval of Service Parties

It is not permissible to put measuring systems into first use without prior reverification except new MID-measuring systems meeting requirements of Art. 7 respecting installation, these shall be reverified for the first time no later than when two years have passed as of the installation of new measuring system.

Measuring systems which are used in accordance with para. 1, Art. 1 shall be reverified every other year.

Reverificartion will be invalidated although the period has not passed if a measuring system fails, a seal is broken, repairs are performed to the measuring system, a measuring system has been tampered with so that its measuring conclusions can be influenced, a measuring system is moved or if errors exceed the double maximum permissible errors as per Art. 13.

The provision of para. 3 notwithstanding a service party who is approved by the Consumer Agency is permitted to break seals and undertake repairs or transportation of a measuring system without reverification being invalidated.  The service party shall seal the measuring system anew by means of his identity and keep reports of what was done and send the Consumer Agency an annual summary.

An approval of a service party, cf. para. 4, is subject to conditions and the decision of the Consumer Agency following upon investigation of his capability and mode of work in order to ensure that measuring results continue to be within the maximum permissible errors in use.  Service party’s volumetric tanks shall have a traceable calibrations.

The Consumer Agency will issue an approval in writing to a service party with further terms and delimitation of permitted repairs.  In case a service party no longer meets the conditions laid down by the Consumer Agency it shall withdraw and invalidate the approval for the service party in accordance with the present Article.

CHAPTER VI

Internal Control, Reverification Parties and Testing Laboratories

Art. 15

General Conditions for Internal Control

It is permissible to use internal control instead of reverifications after having obtained the approval of the Consumer Agency according to the provisions of the present Regulations, cf. Art. 14 of Act No. 91/2006 on Measurements, Measurement Standards and Official Weighers.  This fact notwithstanding new EEC-measuring systems shall obtain reverification prior to being put into use, cf. Art. 5.

Internal control shall ensure correct measurements and that maintenance and tests be undertaken at the correct times and that the proportion of measuring systems which may be supposed to have exceeded permissible error limits as per Chapter IV be acceptable.

Tests of measuring systems subject to internal control shall be in accordance with the provisions of Chapter V and tests shall be performed by a testing laboratory meeting the provisions of Art. 19.

When using internal control instead of reverification an information system shall be applied covering all measuring systems subject to the scope of the present Regulations.  The Consumer Agency shall be granted pertaining information from this system and consumers shall be shown that the measuring systems be subject to internal control with stipulated markings.

The internal control system shall be fully documented in the control and quality manual of the owner of measuring systems.

Art. 16

Application and Proceedings to apply Internal Control

Owners of measuring systems may request the approval of the Consumer Agency that quality system and other formal arrangement of internal control of measuring systems be accepted to replace reverification.

To an application there shall be attached:-

- A control and quality manual on the system for internal control based on IST ISO 9000:2001 as may be applicable.

- Owner’s contract with an accredited inspection body on the pre-inspection of the pertaining internal control.

- A survey of the operation of the system and other information which the Consumer Agency considers necessary for approval, provided that this is not revealed in the control and quality manual.

- A system for internal control shall meet all provisions of Laws and the present Regulations as well as rules which the Consumer Agency lays down and are to ensure correct measurements.

The Consumer Agency shall advise an applicant that a pre-inspection by a accredited inspection body may be undertaken when a satisfactory application and annexec documents are at hand.

The inspection body undertakes inspection and appraisal of a system for the internal control on the basis of rules laid down by the Consumer Agency and which are revealed in the Consumer Agency’s inspection manual for internal control.

In the course of application proceedings for approval of the internal control an applicant is obliged to grant all information about the arrangement of internal control, control manual and other data concerning the operation of the system and to grant all necessary information required in order to assess and give instructions concerning the contemplated internal control.

The Consumer Agency decides upon approval on the basis of an opinion from an accredited inspection body and the improvement which the applicant has effected when applicable.  In case an applicant for internal control meets all conditions determined by the Consumer Agency it will grant permission for the use of internal control to replace reverification against payment of a licensing fee according to tariff laid down by a Minister.

In case the Consumer Agency rejects approval this shall be substantiated in writing.

In case internal control no longer meet the conditions the Consumer Agency shall withdraw the permission for internal control of measuring systems, cf. also the provisions of Art. 17.

Art. 17

Annual Supervision and Reporting

An owner of measuring systems who has obtained the approval of the Consumer Agency for internal control, cf. Art. 15 and 16, shall have a contract with an accredited inspection body concerning annual supervision in conformity with the inspection manual of the Consumer Agency as well as special inspection if applicable.  An accredited inspection body shall render an annual report to the Consumer Agency no later that by 1 March in  respect of the immediate past year concerning all supervision and inspections, conclusions of inspections and decisions which have been made concerning measuring systems.

There shall be recorded adjustments done, all types of break-downs, defects and errors, broken seals of measuring systems.  In addition thereto there shall be recorded defects on the environment of measuring systems.  In other respects the form, classification of deviations and the contents of the report shall be as determined by the Consumer Agency.

The Consumer Agency will confirm no later than by 1 June the extension of the time of validity of permission for internal control against payment of an annual supervisory fee as per a tariff laid down by a Minister.

Art. 18

Reverification Bodies

Parties undertaking reverification of measuring systems as commissioned by the Consumer Agency shall be independent of owners, cf. Art. 3 of the Administrative Act No. 37/1993 and shall be capable as confirmed by accreditation, cf. Art. 4 of Regulations No. 956/2006 on the Mode of Work of Those Undertaking Reverification of Measuring Instruments as commissioned by the Consumer Agency.

Art. 19

Testing Laboratories

Testing laboratories which test measuring systems for owners according to these rules shall be accredited for testings in accordance with Chapters IV and V by an accreditation body being a signatory of the multilateral agreementof EA.

A Testing laboratory may be a reverification body, but shall be independent of owners of measuring systems, cf. Art. 3 of the Administrative Act No. 37/1993 and shall be independent of those being responsible for supervision of the meters and decisions made on the basis of the test results.

CHAPTER VII

Supervision, Market Surveillance, Administrative Resorts et al.

Art. 20

The Task of the Consumer Agency

The Consumer Agency supervises the abidance by the provisions of the present Regulations and undertakes market surveillance in conformity with Directive No. 2004/22/EC on Measuring Instruments and the provisions of Act No. 91/2006 on Measurements, Measurement Standards and Official Weighers.

Art. 21

Administrative Resorts

The implementation of supervision of measuring systems, judicial solutions and penalties for violations of the provisions of the present Regulations are subject to the provisions of Act No. 91/2006 on Measurements, Measurement Standards and Official Weighers.

Art. 22

Fees on Account of Internal Control

The Consumer Agency collects a licensing fee and an annual supervisory charge on account of internal control, cf. Art 16 and 17 and as per a tariff laid down in conformity with the provisions of Art. 32 of Act No. 91/2006 on Measurements, Measurement Standards and Official Weighers.

CHAPTER VIII

Appeal and Means of Complaints

Art. 23

Appeal and Means of Complaints

Decisions made by the Consumer Agency on the basis of the present Regulations can be appealed to the Consumer Appeals Committee which acts on the basis of Art. 4 of Act No. 62/2005 on the Consumer Agency and Consumer Spokesman.

The decision of the Consumer Agency can not be submitted to Courts of Law until a ruling from the Consumer Appeals Committee is available.

CHAPTER IX

Penalties

Art. 24

Penalties

A party who deliberately or inadvertently violates the provisions of the present Regulations shall be subject to monetary fines or imprisonment for up to six months in case of gross violations.

A party giving incorrect or misleading information in connection with decisions or who does not reveal issues of importance for disclosing a Case under the present Regulations shall be subject to fines, unless a heavier penalty applies under Laws.

Those violating the provisions of Chapters III, V and VI shall be subject to fines.

A fine under the present Regulations may be imposed on legal persons in conformity with provisions of Penal Laws on fines for legal persons.

CHAPTER X

Entry into Force, Alignment et al.

Art. 25

Entry into Force and Alignment

The present Regulations are laid down with support in Act No. 91/2006 on Measurements, Measurement Standards and Official Weighers and enter into force forthwith.

At the same time there are repealed Regulations No. 355/1997 on the Reverification of Volume meters for Liquids Other Than Water.

It is permissible to reverify the measuring systems which were taken into use prior to the entry into force of Regulations No. 129/1994 on Measurement Instruments and Methods of Metrological Control as well as measuring systems which have been legally taken into use in accordance with Regulations in force at each given time as of 1994 if these meet pertaining requirements for reverification.

Temporary Provisions

All EEC type approvals which have been issued on the basis of Regulations No. 129/1994 remain in force until their term of validity expires or until these are amended or withdrawn by a legal authority in the European Economic Area.