Regulation regarding the change of the Regulation of 26. June 2002 no 847 relating to fire prevention measures and control

§ 1-3. Definitions

New definition in relation to Portable fire extinguishers:

Portable fire extinguisher: 		Fire extinguisher that meets the requirements in NS-EN 					3.

New definition relating to Smoke detectors:

Approved smoke detector: 		A smoke detector that is in accordance with harmonised 					European product standards.

New definition relating to Additional Equipment:

Additional Equipment: 		A handheld product made for fighting fires, which does 					not meet the minimum requirements regarding size and 					fire fighting capacity for portable fire extinguishers in 					line with NS-EN 3.

§ 2-5. Smoke detectors and portable fire extinguishing equipment in dwellings

The regulation shall read:

The owner of a dwelling is obliged to ensure that the dwelling is equipped with at least one approved smoke detector, situated in a location where it can be heard from all bedrooms when the doors are shut.

## The owner is also obliged to ensure that the dwelling is equipped with

- portable ABC powder based fire extinguisher weighing a minimum of 6 kg

- foam/water based extinguisher containing at least 6 litres, with an effectiveness classification of minimum 21A

- fitted hose reel with an inner diameter of minimum 10 mm, or

- other portable fire fighting equipment with an equivalent fire fighting capacity

The fire extinguishing equipment must be reachable from all rooms.