18.12.02

Forslag til endring av kjøretøyforskriften

Ny § 16-5 skal lyde:

”§ 16-5 Alternativ standard

1. Bestemmelsene i denne paragraf  trer i kraft … … …. Adgangen til å få godkjent og registrert bil med bilbelter etter alternativ standard gjelder også tidligere registrert bil, men ikke bil gruppe M1 med EF-typegodkjenning fra 1.oktober 2001 eller senere.

Adgangen til førstegangsregistrering av bil med bilbelter etter alternativ standard gjelder ikke for bil gruppe M1.

2. Ved typegodkjenning og enkeltgodkjenning kan, på sitteplasser der denne forskrift krever E- eller e-godkjente bilbelter og festepunkter, alternativt godtas belter og fester godkjent etter FMVSS (Federal Motor Vehicle Safety Standards) 209 og 210. Beltene skal være av type som fastsatt i denne forskrift, og det er videre en forutsetning at beltene har dobbel låsemekanisme, dvs. at de låses både ved g-påvirkning på rullen og ved raskt uttrekk.

Tidligere § 16-5 og §16-6 blir nye § 16-6 og § 16-7.”

# Proposal for an amendment to the Norwegian Vehicle Construction Regulations

New § 16-5 shall read:

“§ 16-5 Alternative standard

1. The regulations of this section come into affect … (date of publication). The opportunity to have a vehicle approved and registered with safety belts conforming to an alternative standard  includes previously registered vehicles, but not vehicles of category M1 with EC type approval from 1 October 2001 or later.

The opportunity to have a vehicle approved and registered for the first time with safety belts conforming to an alternative standard does not apply to vehicles of category M1.

2. In connection with type approval and individual approval, in seats where E- or e-approved safety belts and anchorages are required according to this regulation, safety belts and anchorages with FMVSS 209 and 210 approval may alternatively be accepted. The safety belts shall be of a type as laid down in this regulation, and it is further a condition that the safety belts are fitted with double locking mechanism, i.e. that they lock both when exposed to g-force and when pulled vigorously.

Previous §§ 16-5 and 16-6 become new §§ 16-6 and 16-7.”