AMENDMENTS TO:

Regulation of 13 June 2000 concerning the construction, operation, equipment and surveys of fishing vessels 15 metres in overall length (LOA) and over:

I

New § 1-10 paragraph 4 to be read as follows:

(4) Periodical surveyx of radio installations

- For vessels of 24 metres in length (L) and over, or vessels which have a certificate for the trade area bank fishing II or larger, periodical survey shall be undertaken on every anniversary in the certificate period. The survey shall be such as to ensure that the required radio installations fully comply with the requirements of applicable regulations and that the equipment is in good working order.

- For vessels less than 24 metres in length (L) which have a certificate for the trade area bank fishing I or smaller, periodical survey shall be undertaken on every second anniversary in the certificate period. The survey shall be such as to ensure that the required radio installations is working satisfactory and that the equipment is in good working order.

- Periodical radio surveys may take place within a periodof three months before or after the anniversary of the certificate, without any change of date for the next periodical survey.

New footnote to be read as follows:

xFor vessels less than 24 metres in lenght (L) which have a certificate for the trade area inshore fishing or smaller, periodical surveys of radio installations are not required before 1. February 2004.

New § 7-1 paragraph 2 to be read as follows:

- §§ 7-13 and 7-14 shall also apply to existing vessels.

Footnote is to be repealed

New § 7-13 to be read as follows:

(1) Every vessel1shall carry at least one portable two-way VHF radiotelephone apparatus for each survival craft, among them rescue boat. Such apparatus shall conform to the performance standards specified in appendix 4. If a fixed two-way VHF radiotelephone apparatus is fitted in a survival craft it shall conform to the same performance standards as for portable VHF.

(2) Radio life-saving appliances shall at all times comply with the regulations in force concerning EEA approval of maritime radio equipment laid down by Norwegian Post and Telecommunications Authority.

1Ref. § 7-1 paragraph 2).

New § 7-14 paragraph 2 to be read as follows:

Special requirements for vessels 24 metres or above in length (L).

Every survival craft and rescue boat carried on any vessel 24 metres or above in length (L) shall be permanently provided with a radar transponder.

New § 7-14 paragraph 3 to be read as follows:

Special requirements for vessels less than 24 metres in length (L).

- Vessels less than 24 metres in length (L) operating in the trade areas Inshore fishing or Bank fishing I shall be provided with one radar transponder so stowed as to be capable of being quickly moved to a survival craft.

- Vessels less than 24 metres in length (L) operating in the trade area Bank fishing II or a greater trade area shall be provided with one radar transponder on either side of the vessel, so stowed as to be capable of being quickly moved to a survival craft. One of these transponders may be replaced by a manual emergency position-indicating radio beacon capable of operating at 406/121 MHz3. Alternatively, one radar transponder may be carried in such survival craft.

New § 9-1 paragraph 2 to be read as follows:

(1) Unless expressly provided otherwise, this chapter shall apply to new and existing vessels 15

metres in overall length (LOA) and over.

Footnote is to be repealed

New § 9-4 no. 6 to be read as follows:

6.   Of transmitting and, as required by § 10-3 paragraph 3) (radar), receiving signals for locating,

when it has a certificate for the trade area inshore fishing or larger or has a length (L) of 24

metres and over,

New § 9-6 paragraph 1 no. 3 to be read as follows:

- A radar transponder capable of operating in the 9 GHZ band when the vessel has a sertificate for the trade area inshore fishing or larger or has a length (L) of 24 metres and over. The radar transponder shall be

- so stowed that it can be easily utilized, and

- may be one of those required by § 7-14 for survival craft.

New § 9-6 paragraph 1 no. 4 to be read as follows:

- A receiver capable of receiving international NAVTEX service broadcasts if the vessel is engaged on voyages in any area in which an international NAVTEX service is provided. For vessels less than 24 metres in length (L) with a certificate for the trade area inshore fishing or smaller, such a reciever will not be required if the vessel can obtain a weather announcement sevice by other means.

New § 9-6 paragraph 1 no. 6 to be read as follows:

- A satellite emergency position-indicating radio beacon (EPIRB) when the vessel has a certificate for the trade area inshore fishing or larger or when the vessel has a lenth (L) of 24 metres and over, which shall be:

- capable of transmitting a distress alert either through the polar orbiting satellite service operating in the 406 MHz band or, if the vessel is engaged only on voyages within Immarsat coverage, through the Immarsat geostationary satellite service operating in the 1.6 GHz band,

- installed in an easily accesable position,

- ready to be manually released and capable of being carried by one person into a survival craft,

- capable of floating free if the vessel sinks and of being automatically activated when afloat, and

- capable of being activated manually.

For vessels engaged exclusevely on voyages in sea area A1 this requirement may be replaced with emergency position-indicating radio beacon required by § 9-7 paragraph 3).

New § 9-7 paragraph 5 to be read as follows:

(5)  For vessels less than 24 metres in length (L) which has a certificate for inshore fishing, the    requirements in paragraph one to four above do not apply if it exists a VHF radio installation which can transmit and receive as described in § 9-6 paragraph 1) no. 1 and a portable two-way VHF as described in § 7-13.

New § 12-3 paragraph 2 to be read as follows:

For existing vessels of 24 metres in length (L) and over it is the owner`s or skipper`s resposibility to ensure that radar transponders are fitted at the first regular inspection after the entry into force1 of this regulation of inflatable liferafts in accordance with § 7-16 paragraph 7), cf. § 7-14.

New footnote to be read as follows:

1For existing vessels of 24 metres in length (L) and over, but less than 45 metres in length (L), this regulation enters into force 1. February 2003. For existing vessels of 45 metres in length (L) and over, this regulation entered into force 1. July 2000.

II

For vessels which have a certificate for the trade area bank fishing I and larger and for vessels of 24 metres in length (L) and over, § 1-10 paragraph 4) in this regulation enters into force on xx.xxxx 2002. From the same time will the existing § 1-10 paragraph 4) in regulation no. 660 of 13. June 2000 be repealed for all vessels.

For existing vessels of 24 metres in length (L) and over, but under 45 meters (L), this regulation enters into force 1. February 2003 with the exeption of § 1-10 paragraph 4). From the same time will regulation no. 1242 of 22 December 1993 be repealed for vessels of 24 metres in length (L) and over, and §5a in regulation no. 709 of 15 October 1991 will be repealed for vessels of 24 metres in length (L) and over.

For existing vessels of 15 metres in overall length (LOA) and over, but under 24 metres in length (L), this Regulation enters into force 1. February 2004 with the exeption of § 1-10 paragraph 4) for vessels which have a certificate for the trade area bank fishing I or larger. From the same time will regulation no. 1242 of 22 December 1993 be repealed for vessels of 15 metres in overall length (LOA) and over, and § 5a in regulation no. 709 of 15 October 1991 will be repealed for vessels of 15 metres in overall length (LOA) and over.