EEA INFORMATION PROCEDURE ON DRAFT TECHNICAL REGULATIONS

(ANNEX II, CHAPTER XIX, 1. EEA AGREEMENT)

ACKNOWLEDGEMENT OF RECEIPT OF DRAFT TEXT FOR NOTIFICATION 2002/9006/N

COMMUNICATION FROM THE EFTA SURVEILLANCE AUTHORITY

TO :	EEA-EFTA CENTRAL UNITS

EFTA SECRETARIAT

EUROPEAN COMMISSION

2002/9006/N

THE TEXT OF THE DRAFT TECHNICAL REGULATION CORRESPONDING TO THIS NOTIFICATION WAS RECEIVED BY THE EFTA SURVEILLANCE AUTHORITY ON 08.03.2002. THE STANDSTILL PERIOD OF THREE MONTHS PROVIDED UNDER ARTICLE 9 OF DIRECTIVE 98/34/EC, AS ADAPTED IN THE EEA AGREEMENT, THEREFORE COMES TO AN END ON 10.06.2002.

THE DRAFT TEXT IS ATTACHED TO THIS MESSAGE.

EEA INFORMATION PROCEDURE ON DRAFT TECHNICAL REGULATIONS ACCORDING TO

DIRECTIVE 98/34/EEC (ANNEX II, CHAPTER XIX, 1. EEA AGREEMENT)

TO:	ESA

1.

2.	N

3.A.	ROYAL MINISTRY OF TRADE AND INDUSTRY,

Department for Industrial and Trade Issues

P.O. BOX 8014 Dep

N-0030  OSLO

3.B.	The Norwegian Maritime Directorate

P.O. Box 8123 Dep

N-0032  OSLO

+47 22 45 45 00/22 45 44 42

4.	2002/9006/N

5.	In English: draft regulation to amend Regulation of 15 September

1992 concerning the Construction of passenger Ships, cargo ships and

Barges.("amending § 36 - Towing and anchor-handling equipment")

In Norwegian: Utkast til endring av forskrift av 15 september 1992 nr 695 om

bygging av passasjer,- lasteskip og lektere.( endring av " § 36 - Slepe- og

ankerhåndteringsutstyr")

6.	Towing and anchor handling equipment onboard anchorhandling vessels.

7.

8.	The revised § 36 requires:

Automatic spooling device on wince drums used for anchor handling. This new

requirement concerns both new and existing ships that will be upgraded to

handle anchors on deeper waters than it was originally built for, see 1.

Sentence lit. d).

Anchorhandling vessels shall be arranged to release torsinal forces in the

wire under controlled conditions.

Towing pins and chain/wire stoppers on new and existing ships to be fitted

with audible alarms.

Existing ships must comply with these provisions not later than 1. July

2004.

9.	The aim of the draft is to reduce risk of accident and minimise

potential consequences of an accident. In May 2001, a man lost his life on

the anchor handling ship "Viking Queen". The Norwegian Maritime Directorate

and represents of the maritime industry and shipping companies held a

meeting in order to improve safety on ships built for anchor handling

purposes.  The general opinion was that something had to be done to improve

safety.

10.	There are no international regulations regarding anchor-handling

equipment. The International Maritime Organisation (IMO) has formed

guidelines for safe ocean towage (MSC/Circ. 884, 1998). These guidelines are

not mandatory, and they are not implemented into Norwegian national law. The

draft however implements some of the requirements from the guidelines, see

4. Sentence, lit. f) and g).

11.	No

12.

13.	No

14.	No

<<Utkast til ny § 36 i byggeforsk..doc>>  <<(eng) ny  36  (070302)_.doc>>