|  |  | Sjøfartsdirektoratet Norwegian Maritime Directorate |  |
| --- | --- | --- | --- |

ATTACHMENT 1

### Draft regulation concerning amendment to Regulation of 28 March 2000 No. 305 concerning surveys, construction and equipment of passenger ships engaged on domestic voyages.

Laid down by the Norwegian Maritime Directorate pursuant to the Act of 9 June 1903 No. 7 relating to Public Control of the Seaworthiness of Ships, etc. §§ (Sections) 1, 11, 35, 41a, 47, 48, 54a, 55, 80, 94, 96, 97, 100, and 106, cf. Royal Decree of 12 October 1962, Royal Decree of 5 April 1963, Royal Decree of 1 December 1978 and Formal Delegation of 15 January 1979 authorizing the Norwegian Maritime Directorate to lay down regulations pursuant to the Seaworthiness Act, ref. the EEA Agreement Annex XIII No. 56f (Council Directive 1998/18/EC),  ref. the EEA Agreement Annex II (Council Directive 1998/34/EC).

I

The following amendments are made to the Regulation of 28 March 2000 No. 305 concerning surveys,  construction and equipment of passenger ships engaged on domestic voyages:

§ 8 subsection 1 b) should read:

- The provisions of chapter IV, including the 1988 GMDSS amendments, and chapters V and VI of the 1974 Solas Convention, as amended per 17 March 1998.

Chapter IV of SOLAS 1974 applies to passenger ships engaged on domestic voyages in Norway, with the following exceptions and interpretations:

Passenger ships Classes B and C

The following requirements for radio installations do not apply to Class B or C vessels:

- distress panel (SOLAS 1974-R.IV/6.4). This requirement is considered fulfilled by the alarm button on the vessel’s VHF/DSC radio installation together with a remotely activated satellite EPIRB (SOLAS 1974-R.IV/7.1.6), or by an additional EPIRB installed in the wheelhouse near the conning position. The latter may either be a float-free or a manually activated type,

- distress alarm panel (SOLAS 1974-R.IV/6.6)

#### Passenger ships Class D

The following requirements for radio installations do not apply to Class D vessels:

- secondary source of alerting (SOLAS 1974-R.IV/4.1.1). This requirement is considered fulfilled by the vessel’s VHF/DSC radio installation (SOLAS 1974-R.IV/7.1), together with the number of two-way radiotelephone apparatus provided for search and rescue purposes as required by regulation III/6.2.1 of SOLAS 1974.

- NAVTEX receiver (SOLAS 1974-R.IV/4.1.7 and SOLAS 1974-R.IV/7.1.4),

- distress panel (SOLAS 1974-R.IV/6.4).  This requirement is considered fulfilled by the alarm button of the vessel’s VHF radio installation,

- distress alarm panel (SOLAS 1974-R.IV/6.6),

- satellite EPIRB (SOLAS 1974-R.IV/7.1.6).

§ 8 new subsection 2 b) should read:

- Additional safety requirements, equivalents, exemptions and safety measures.

- Annex I - regulation II-1/B/17-1/1.1 (watertight integrity from the car deck (bulkhead deck) to spaces below) does not apply provided all accesses that lead to spaces below the bulkhead deck have a lowest point which is not less than 600 mm above the bulkhead deck and :

- all accesses are closed by weathertight doors with centralized closing means, and

- alarmed and indicated to the navigational bridge.

- Annex I - regulation II-1/D/3.1 (concerning emergency source of electrical power) does not apply to ships constructed with two fully redundant machinery spaces, separated by at least two watertight and fire-safe compartments with a combined length equal to L/4, provided that the generators in either machinery space meet the provisions in regulation II-1/D/3.2 to 3.5.

- Annex I - regulation II-2/A/1.1 (concerning fireman's outfit) does not apply to Class C or D ships operating on short routes, provided that:

- the ship has no accommodation below the (bulkhead) deck,

- the ship has no passenger cabins,

- the ship's passenger accommodation has direct access to the open deck forward and aft,

- the ship has separate and redundant propulsion and steering systems.

- Annex I - regulation III/5-1.3.1 (Fast rescue boats). The testing requirements according to MSC/Circ.809, as amended, do not apply to Class D ro-ro passenger ships.

- Annex I - regulation III/5-2 (Helicopter landing and pick-up areas) does not apply to Class C or D ro-ro passenger ships operating on short routes where the distance to the nearest port never exceeds one hour provided there is a helicopter and pick-up area available at the nearest port.

§ 8 subsection 2 b) should be renumbered as subsection 2 c).

§ 8 new subsection 3 d) should read:

- Additional safety requirements, equivalents, exemptions and safety measures.

i)	Annex I - regulation II-1/B/17-1/1.1 (watertight integrity from the car deck (bulkhead deck) to spaces below) does not apply provided all accesses that lead to spaces below the bulkhead deck have a lowest point which is not less than 600 mm above the bulkhead deck and :

- all accesses are closed by weathertight doors with centralized closing means, and

- alarmed and indicated to the navigational bridge.

- Annex I - regulation II-1/D/3.1 (concerning emergency source of electrical power) does not apply to ships constructed with two fully redundant machinery spaces, separated by at least two watertight and fire-safe compartments with a combined length equal to L/4, provided that the generators in either machinery space meet the provisions in regulation II-1/D/3.2 to 3.5.

- Annex I - regulation III/5-1.3.1 (Fast rescue boats). The testing requirements according to MSC/Circ.809, as amended, do not apply to Class D ro-ro passenger ships.

- Annex I - regulation III/5-2 (Helicopter landing and pick-up areas) does not apply to Class C or D ro-ro passenger ships operating on short routes where the distance to the nearest port never exceeds one hour provided there is a helicopter and pick-up area available at the nearest port.

§ 8 subsection 3 d) should be renumbered as § 8 subsection 3 e).

II

This regulation enters into force on ……….