Draft regulations concerning amendments to Regulations of 17 December 1986 No. 2318 concerning the construction and equipment of living quarters on mobile offshore units

In § 1 Definitions, existing subsection 4 up to and including subsection 7 should be

deleted.

In § 1 Definitions, new subsections 4, 5 and 6  should read:

"4. Living quarters: Those areas of the unit which are described in these regulations.

5. Mustering station: A meeting place for entering lifeboats and liferafts.

6. Emergency station: A meeting place for personenel who are assigned special duties in an emergency situation"

§ 2 Application is amended (heading and provisions) and should read:

"§ 2 Scope of application

- These regulations apply to mobile offshore units which are or will be registered in a Norwegian ship register.

- Mobile offshore units which are registered in a Norwegian ship register may, until the next certificate issue, comply with the requirements that applied at the time of the last certificate issue."

§ 3 Responsibility should read:

"§ 3 Responsibility

The owner and the platform manager are responsible for compliance with the provisions of these regulations1.

_______________

1  See also Regulations of 2 March 1999 No. 394 concerning a Safety Management System for mobile offshore units."

§ 4 Drawings, etc. is amended (heading and provisions) and should read:

"§ 4 Documentation

The owner shall be able to document that the requirements of these regulations are complied with. Documentation shall be sent to the Norwegian Maritime Directorate on request. The contents, scope  and type of documents and the time of submission shall be decided by the Norwegian Maritime Directorate."

§ 5 Approval - system audit - verification is repealed.

In § 6 General requirements, subsection 1 should read:

"1. Living quarters shall be so located as to be adequately separated from danger areas on the unit. Living quarters shall not be adjacent to explosion-hazardous areas and shall comply with the requirements of the regulations in force concerning precautionary measures against fire and explosion on mobile offshore units."

In § 6 General requirements, the first sentence of subsection 3 should read:

"Living quarters shall be provided with a sufficient number of exits/staircases which provide easy access to the mustering stations."

In § 6 General requirements, new subsection 5 should read:

"5. Living quarters shall be so arranged as to ensure that a proper hygienic standard is maintained."

In § 6 General requirements, existing subsections 5 to 9 should be renumbered as 6 to 10.

In § 7 Structural requirements, the second sentence of subsection 1 should read:

"The insulation shall have a K-value not exceeding 0.50."

In § 7 Structural requirements, subsection 3 should read:

"3. All materials used in the living quarters shall have a surface which makes them easy to keep clean."

In § 7 Structural requirements, subsection 6 should read:

"6. Bulkheads and ceilings in sanitary rooms shall be of steel or equivalent material and be insulated against external bulkheads."

In § 8 Corridors, exits, emergency exits and escape routes, subsection 4 should read:

"4. All doors and hatches in emergency exits shall open in the direction of the escape route and shall be easily opened from each side by one person. Doors and hatches with dog bolts shall be operated centrally. Doors to cabins shall be equipped with a kick-through panel or be unlockable.

In § 9 Ventilation, first sentence of subsection 1 should read:

“1.  The living quarters shall be adequately ventilated by mechanical ventilation means and be overpressured with 50 Pascal compered with the surroundings.

In § 12 Galley and provision room, subsection 2 should read:

"2. The floor of the galley shall have a no-skid surface which is easy to keep clean. The floor-wall junction shall be so designed as to make it easy to keep clean. The floor shall be provided with a sufficient number of water drains, at least one on each side at the lowest point in all normal heel conditions."

In § 12 galley and provision room, last sentence of subsection 6 should read:

“The temperature of the refrigerated room shall be minus 18º C or lower.”

In § 12 galley and provision room, last sentence of subsection 7 should read:

The temperature of the cold storage rooms shall be between minus 1º and plus 4º C.

In § 12 galley and provision room, subsection 9 should read:
It shall be possible to drain the refrigerated rooms and the cold storage rooms.

In § 13 Cabins, subsection 6 should be deleted.

In § 14 Furniture and other equipment for cabins, subsection 7 should read:

"7. In cabins intended for more than one person, berths shall be furnished with curtains."

In § 16 Health office, subsection 2 should read:

"2. The health office shall be so furnished and equipped that all medical examination and treatment may be carried out in a medically safe way."

In § 16 Health office, subsection 4 should be deleted.

In § 17 Sanitary rooms, changing rooms, etc., subsection 9 should read:

"9. Adjacent to the changing room, there shall be wash basins, showers, water closets and urinals in such number as is deemed to be reasonable considering the number of people assumed to be using the room at the same time. If several smaller changing rooms are arranged, such rooms shall be provided with at least one wash basin, one shower and one water closet."

§ 19 Deviations should read:

"The Norwegian Maritime Directorate may, in individual cases and upon written application, deviate from the requirements of these regulations. There must be special reasons that make the deviations necessary and they must be justifiable in terms of safety. If the requirements of the coastal state and the requirements of these regulations are irreconcilable, the Norwegian Maritime Directorate may deviate from the requirements insofar as safety considerations allow. Deviations must not contravene international agreements to which Norway has acceded."

§ 20 Penalty should read:

"Wilful or negligent violation of these regulations is punishable by fines pursuant to the General Civil Penal Code of 22 May 1902 No. 10, § 339 subsection 2, ref. § 48a and § 48b, unless a more severe penalty is applicable pursuant to any other statutory provision."

Note: The ANNEX to these regulations is repealed and deleted.