11.07.2002

EEA INFORMATION PROCEDURE ON DRAFT TECHNICAL REGULATIONS ACCORDING TO

DIRECTIVE 98/34/EEC (ANNEX II, CHAPTER XIX, 1. EEA AGREEMENT)

TO:	ESA

1.

2.	N

3.A.	ROYAL MINISTRY OF TRADE AND INDUSTRY,

Department for Industrial and Trade Issues

P.O. BOX 8014 Dep

N-0030  OSLO

3.B.	The Norwegian Maritime Directorate

P.O. Box 8123 Dep

N-0032  OSLO

+47 22 45 45 00/22 45 44 42

4.	2002/9016/N

5.	In Norwegian: Utkast til forskrift om endring i forskrift av 31.

Januar 1984 nr. 227 om sikringstiltak mot brann og eksplosjon på flyttbare

innretninger

In English: Draft regulation concerning amendments to regulation of

31 January 1984 No. 227 concerning precautionary measures against fire and

explosion on mobile offshore units

6.	Mobile Offshore Units (MOUs)

7.	 Not relevant

8.

*	The regulation and the draft amendment apply to Norwegian flagged

Mobile Units (MOUs) only.

*	The draft implies that the most recently adopted requirements in

force will apply to all MOUs, irrespectively of age. Previous approved MOUs

will have to make necessary upgrades as a result of this amendment.

*	Content of some of the definitions is proposed changed to harmonise

the definitions in all the regulations concerning MOUs.

*	Editorial amendments and amendments to the administrative provisions

regarding phasing out approval/type approval/detail approval made by the

Norwegian Maritime Directorate. The only formal approval proposed given,

will be the Maritime Certificates for the MOU issued when all matters are

dealt with. However, where appropriate, certified equipment is proposed

required.

*	Content of definitions in §1, new subsections 8,  9, 10, 11, 12 and

13 is proposed amended to harmonize with the IMO FTP code (International

Code for Application of Fire Test Procedures)

*	§ 1 new subsection 14, 'H' class divisions is proposed defined

*	In § 5 subsection 5 it is proposed that when hot work is planned, a

hot work permission should be issued prior commencement.'

*	In § 6 subsection 3 the capacity requirement for fire pumps is

proposed linked to dimensioning design fire.

*	In § 10 requirements based on  IMO documents regarding detail

requirements for fixed fire extinguishing system of gas, water-spray and

high-expansion type, are proposed

*	In §19 requirements which refer to the FTP-Code, are proposed

included.

*	In § 19 subsection 12 to 18 requirements for ventilation ducts are

rearranged and specified better to clarify the difference between danger of

explosion and danger of fire

*	In § 19 subsection 18 and 19 it is proposed more stringent

requirements; fire dampers should be both automatic and locally operated.

*	In § 23 more stringent requirements for the communication system are

proposed

*	In § 26 it is proposed that the deluge system (connected to the

equipment for release of anchor lines) should also be functional after a

level 2 emergency shout down

*	Appendix 3 and appendix 4 to the regulations are proposed repealed

9.

*	The proposed amendments will bring the MOUs to a higher, more

uniform and predictable level of safety, which is required for drilling at

the Norwegian Continental Shelf.

*	The technical/operational amendments are proposed to either update

the regulations or make the requirement itself more predictable. When

possible, requirements given in IMO documents are proposed implemented by

referring to the document in the text.

*	By avoiding detail approvals, liberty to pay more attention to

critical areas is achieved.

10.

*	FTP-Code:  International Code for Application of Fire Test

Procedures

*	MSC/Circ. 766

*	MSC/Circ. 668

*	MSC/Circ. 728

*	IMO res. A.754(18)

*	EN-54

*	IEC 92-504

*	ISO 834

11.	No

12.	None

13.	No

14.	No

<<brann -engelsk.doc>>  <<Brann -norsk.doc>>