Draft regulations concerning amendments to Regulations of 16 December 1993 No. 1200 concerning the installation and use of radio equipment on mobile offshore units

In "Preface", the fourth paragraph should read:

"The requirements regarding GMDSS are mandatory for new mobile offshore units from the date of entry into force of the regulations. The GMDSS requirements became mandatory for existing units on 1 February 1999.

In "Preface", the first item of the fifth paragraph should read:

"1. Radio equipment for use in survival craft. Requirements for such equipment have been given in Regulations of 9 September 1991 No. 702 concerning life-saving appliances and evacuation on mobile offshore units (§ 11)."

§ 1 Application is amended to read:

"§ 1 Scope of application

- These regulations apply to mobile offshore units which are or will be registered in a Norwegian ship register.

- Mobile offshore units which are registered in a Norwegian ship register may, until the next certificate issue, comply with the requirements that applied at the time of the last certificate issue."

In § 2 Definitions, existing subsections 2 and 3 are deleted.

In § 2 Definitions, existing subsections 4, 5, 6, 7, 8, 9, 10, 11, 12, 13 are renumbered as

subsections 2, 3, etc. up to and including 11.

§ 3 Responsibility should read:

"The owner and the platform manager are responsible for compliance with the provisions of these regulations1.

______________

1  See also Regulations of 2 March 1999 No. 394 concerning a Safety Management System for mobile offshore units."

§ 4 Departure from regulation requirements is amended (heading and provisions) and

should read:

"§ 4 Deviations

The Norwegian Maritime Directorate may, in individual cases and upon written application, deviate from the requirements of these regulations. There must be special reasons that make the deviations necessary and they must be justifiable in terms of safety. If the requirements of the coastal state and the requirements of these regulations are irreconcilable, the Norwegian Maritime Directorate may deviate from the requirements insofar as safety considerations allow. Deviations must not contravene international agreements to which Norway has acceded."

The heading of Chapter III  -  Documentation, approval, survey and certification  -  is

amended to read:

"Chapter III -  Documentation, survey and certification"

§ 5 Documentation should read:

"The owner shall be able to document that the requirements of these regulations are complied with. Documentation shall be sent to the Norwegian Maritime Directorate or anyone authorized1 by the Norwegian Maritime Directorate on request. The contents, scope and type of documents and the time of submission shall be decided by the Norwegian Maritime Directorate or anyone authorized by the Norwegian Maritime Directorate.

__________

1  According to the agreement in force concerning assistance between Telenor A/S and the Norwegian Maritime Directorate, Telenor A/S has such authority.

§ 6 Approval - system audit - verification is repealed.

In § 7 Survey and certification, the sentence in subsection 2(a) should read:

"a) Regulations of 9 September 1991 No. 702 concerning life-saving appliances and evacuation on mobile offshore units (§ 11)."

In § 7 Survey and certification, the following note should be added:

" According to the agreement in force concerning assistance between Telenor A/S and the Norwegian Maritime Directorate, Telenor A/S is authorized to carry out surveys and issue Mobile Unit Safety Radio Installation Certificates."

In § 9 Requirements for equipment, in subsection 3.2 the phrase

"Civil Aviation Administration" should be replaced by "Norwegian Civil Aviation Authority".

In § 9 Requirements for equipment, the last note should read:

"4 This recommendation is printed in the publication Excerpts from the Norwegian Passenger and Cargo Ship Legislation, etc."

In § 10 Requirements for personnel and watchkeeping first sentence of  subsection 3

should read:

3. One of the persons holding a certificate as required by subsection 1 shall be designated to have primary responsibility at all times for safety radio communication to and from the unit, and watchkeeping on all relevant distress and safety frequencies in accordance with the provisions of the MODU-Code (cf. the provisions of SOLAS 74/78 Chapter IV, Regulation 12)

§ 11 Existing units is repealed.

§ 13 Penal provision should read:

"Wilful or negligent violation of these regulations is punishable by fines pursuant to the General Civil Penal Code of 22 May 1902 No. 10, § 339 subsection 2, ref. § 48a and § 48b, unless a more severe penalty is applicable pursuant to any other statutory provision."