Draft regulations concerning amendments to:

Reads:

Regulations of 13 January 1986 No. 32 for the use of radioactive sources on board Norwegian drilling platforms and other mobile drilling units

Should read:

Regulations of 13 January 1986 No. 32 for the use of radioactive sources on board mobile offshore units

In § 1 Definitions, existing subsection 1.1 is deleted. New subsection 1.1 should read:

"1.1.  Mobile offshore unit: Mobile platform, including drilling ships, carrying equipment for drilling for subsea petroleum deposits, and mobile platforms used for purposes other than drilling for subsea petroleum deposits."

In § 1 Definitions, subsection 1.2 is amended to read:

"1.2. Platform manager: The senior person in command on board a mobile offshore unit."

§ 2 Application is amended (heading and provisions) to read:

"§ 2  Scope of application

1. These regulations shall apply to mobile offshore units which are or will be registered in a Norwegian ship register.

2. Mobile offshore units which are registered in a Norwegian ship register may, until the next certificate issue, comply with the requirements that applied at the time of the last certificate issue."

§ 3 Responsibility should read:

"The owner and the platform manager are responsible for compliance with the provisions of these regulations1.

______________

1 See also Regulations of 2 March 1999 No. 394 concerning a Safety Management System for mobile offshore units."

The heading of § 4 is amended to read:

"§ 4 Application for permission concerning the transportation, storage and use of radioactive sources on board mobile offshore units"

In § 4, the first sentence should read:

"1. The owner shall obtain a written permission from the Directorate before the transportation, storage or use of radioactive sources on board mobile offshore units."

In § 5 Transportation, storage and use of radioactive sources, subsections 2.1, 2.2, 2,3, 2.4 and 3.1, 3.3 should read:

"2.1. Transportation to and from a mobile offshore unit shall normally be effected by ship¹.

2.2. Transportation containers shall satisfy the IAEA’s (International Atomic and Energy Agency) requirements.

2.3. During transfer of transportation containers from supply vessels to mobile offshore units, special precautions shall be made in order to prevent the loss of containers. The platform manager shall make certain that the transfer is carried out under special supervision.

2.4. If transportation has to be effected by helicopter,² the sources shall be placed as decided by the Civil Aviation Authority in order to make landing or take off possible."

(…)

"3.1. The storage of radioactive equipment, as well as the design of rooms for such storage, shall be according to guidelines issued by the Norwegian Radiation Protection Authority³."

(…)

"3.3  The storage room shall kept locked and marked with the standard (international) warning sign against ionizing radiation with appropriate text. Workplaces or off-duty quarters shall not be submitted to radiation levels exceeding the maximum levels given in the guidelines of the Norwegian Radiation Protection Authority³."

In § 5 Transportation, storage and use of radioactive sources, the notes (¹, ² & ³) should

read:

"¹ Transport of dangerous materials on supply vessels to and from installations on the Norwegian continental shelf is regulated by Regulations of 21 May 1987 No. 406 concerning carriage by ship of special or dangerous cargoes in bulk or as packaged goods, part IV.

² With regard to helicopter transportation, regulations concerning the conveyance of goods in aircraft, laid down by the Civil Aviation Administration (now the Civil Aviation Authority) on 15 May 1979 (latest amendment: 1 April 1997) shall apply. Special reference is made to subsection 8 concerning dangerous goods. Reference is otherwise made to ICAO doc. 9284 – AN/905: «Technical instructions for the safe transport of dangerous goods by air»:

³ Reference is made to guidelines («Strålevernheftene») issued by the Norwegian Radiation Protection Authority, e.g. guideline no. 13b; «Vilkår for strålevern ved brønnlogging» (1997) and guideline no. 20 «Vilkår om strålevern ved industriell radiografi» (1999)."

In § 7 Individual dosimetry, the last sentence (in parentheses) is deleted.

§ 12 Deviations should read:

"The Norwegian Maritime Directorate may, in individual cases and upon written application, deviate from the requirements of these regulations. There must be special reasons that make the deviations necessary and they must be justifiable in terms of safety. If the requirements of the coastal state and the requirements of these regulations are irreconcilable, the Norwegian Maritime Directorate may deviate from the requirements insofar as safety considerations allow. Deviations must not contravene international agreements to which Norway has acceded."

§ 13 Penal provisions should read:

"Wilful or negligent violation of these regulations is punishable by fines pursuant to the General Civil Penal Code of 22 May 1902, § 339 subsection 2, ref. §§ 48a and 48b, unless a more severe penalty is applicable pursuant to any other statutory provision."