12.08.2002

EEA INFORMATION PROCEDURE ON DRAFT TECHNICAL REGULATIONS ACCORDING TO

DIRECTIVE 98/34/EEC (ANNEX II, CHAPTER XIX, 1. EEA AGREEMENT)

TO:	ESA

1.

2.	N

3.A.	ROYAL MINISTRY OF TRADE AND INDUSTRY,

Department for Industrial and Trade Issues

P.O. BOX 8014 Dep

N-0030  OSLO

3.B.	Norwegian Maritime Directorate

Offshore Department

P.O.Box 8123 Dep.

N-0032  OSLO

Tel.: +47 22454500

4.	2002/9035/N

5.	Draft regulation concerning amendments to regulation of  9 September 1991

no. 702 concerning life-saving appliances and evacuation on mobile offshore

units

6.	Mobile Offshore Units (MOUs)

7.

8.

The regulation and the draft amendment apply to Norwegian flagged Mobile

Units (MOUs) only.

The draft implies that the most recently adopted requirements in force will

apply to all MOUs, irrespectively of age. Previous approved MOUs will have

to make necessary upgrades as a result of this amendment.

Content of some of the definitions is proposed changed to harmonise the

definitions in all the regulations concerning MOUs.

§§ 9-12 The IMO LSA-code is proposed implemented by referring to its

requirements directly.

§ 12 subsection 4 e) Fast rescue boats are proposed accepted launched and

hosted either by davit according to LSA-code or by deck crane

§§ 14-18, the requirements for numbers and location of life-saving equipment

are harmonized with the MODU-Code for mobile offshore drilling units, are

proposed.

Editorial amendments and amendments to the administrative provisions

regarding phasing out approval/type approval/detail approval made by the

Norwegian Maritime Directorate. The only formal approval proposed given,

will be the Maritime Certificates for the MODU issued when all matters are

dealt with. However, where appropriate, certified equipment is proposed

required.

9.

The proposed amendments will bring the MOUs to a higher, more uniform and

predictable level of safety, which is required for drilling at the Norwegian

Continental Shelf.

Need to update the regulations based on new international regulations, i.e.

the LSA-Code. For mobile drilling units, compliance with MODU-Code with

regard to numbers and location of life-saving equipment, is demand.

Acceptance of use of deck cranes for fast rescue boat is based on the fact

that MOUs may have suitable deck cranes onboard

Other technical/operational amendments are proposed to either update the

regulations or make the requirement itself more predictable

By avoiding detail approvals, liberty to pay more attention to critical

areas is achieved.

10.

LSA-code: International Life-Saving Appliance Code, Resolution MSC.48(66)

MODU-Code: Code for the construction and equipment of mobile offshore

drilling units 1989, including 1991 amendments.

MSC/Circ. 809: Recommendation for canopied reversible liferafts,

automatically self-righting liferafts and fast rescue boats, including

testing, on ro-ro passenger ships

MSC/Circ.922 : Recommendations on performance standards and tests for

thermal protective lifejackets (TP-lifejackets)

11.	No

12.

13.	No

14.	No