EEA INFORMATION PROCEDURE ON DRAFT TECHNICAL REGULATIONS ACCORDING TO

DIRECTIVE 98/34/EEC (ANNEX II, CHAPTER XIX, 1. EEA AGREEMENT)

TO:	ESA

1.

2.	N

3.A.	ROYAL MINISTRY OF TRADE AND INDUSTRY,

Department for Industrial and Trade Issues

P.O. BOX 8014 Dep

N-0030  OSLO

3.B.	The Norwegian Maritime Directorate

P.O. Box 8123 Dep

N-0032  OSLO
	+47 22 45 45 00/22 45 44 42

4.	2002/9038/N

5.	DRAFT PROPOSAL FOR AMENDMENTS TO REGULATIONS OF 13 JUNE 2000 CONCERNING THE CONSTRUCTION, OPERATION, EQUIPMENT AND SURVEYS OF FISHING VESSELS 15 M IN OVERALL LENGTH (LOA) AND OVER

6.	Fishing vessels between 15 and 24 metres in length and related equipment.

7.

8.	This notification concerns the regulation specified in item 5 above. This draft proposal contains provisions for vessels with length between 15 and 24 metres. These provisions will to a large extend be similar to provisions laid down in the Commission Directive 2002/35 concerning vessels above 24 meters. The proposed amendment will only apply to Norwegian flagged vessels:

§ 1-12 subsection 2 and subsection 3 second sentence about minimum freeboard.

§ 2-9, subsection 4 about ventilators to engine room.

§ 3-2, subsection 1 no 4 about stability criteria for fishing vessels with a hull similar to offshore supply vessels.

§ 3-2, subsection 3 about permanent ballast.

§ 4-10, subsection 7, no 1 last sentence about fitting to flexible pipes.

§ 5-2, subsection 3 no 5, subsection 4 no 4 last sentence and subsection 6 no 3 last sentence about requiring tests of prototypes.

§ 7-3 about evaluation, testing and approval of life-saving appliance and arrangements. Life-saving appliances and arrangements on board vessels of 15 metres in length and above constructed after 1 January 2003 should be tested, to confirm that they comply with the requirements of Council Directive 96/98/EC on marine equipment which includes the IMO Recommendations on Testing of Life-Saving Appliances.

9.	Regulations for vessels between 15 and 24 metres will, when adopted in the new regulation, follow the same structure as vessels above 24 metres, which is the structure laid down in the Torremolinos Protocol, as modified by Commission Directive 2002/35. To a large extent the draft proposals are only maintaining present requirements, and it makes sense to harmonise our regulation concerning fishing vessels. Fewer regulations and the same legal structure for all vessels over 15 meters will presumably make it easier for the final user.

10.	Commission Directive 2002/35.

Regulation of 13 June 2000 concerning the Construction, Operation, Equipment and Surveys of Fishing vessels 15 m in overall length (LOA) and over.

11.	No

12.

13.	No

14.	No