REGULATION CONCERNING AMENDMENT TO REGULATIONS OF 13 JUNE 2000 NO. 660 CONCERNING THE CONSTRUCTION, OPERATION, EQUIPMENT AND SURVEYS OF FISHING VESSELS 15 M IN OVERALL LENGTH (LOA) AND OVER

Laid down by the Norwegian Maritime Directorate on ………. pursuant to the Act of 9 June 1903 No. 7 relating to Public Control of the Seaworthiness of Ships, etc., § 1, § 35, § 41, § 41a, § 42, § 46, § 47, § 48, § 50, § 52, § 54a, § 56, § 59, and § 106, ref. Royal Decree of 5 April 1963 No. 9 and Royal Decree of 1 December 1978 No. 1, ref. para. 147 of Annex XIII to the EEA Agreement (Council Directive 2002/35/EC) (1998/34/EC)

§ 1-12
Freeboard

The Section should read:

(1)	Summer freeboards determined from the surface of the working deck in the side amidships shall correspond to the maximum permissible operating draught, ref. § 3-13, and shall not be less than zero. The winter freeboard is the summer freeboard increased by 25 mm.

(2)	For vessels constructed after 1 January 2003, the freeboard shall be at least 300 mm.

3)	Regardless of the date of build of the vessel, the freeboard of vessels with a shelter deck and, where applicable, a bilge system in accordance with § 2-16 first paragraph, subparagraphs 1 and 2, shall be in accordance with the first paragraph. Vessels with a shelter deck and a drainage arrangement in accordance with § 2-16 first paragraph, subparagraphs 4 and 5, shall have freeboard as provided in the second paragraph.

(4)	The size of the freeboard shall be determined by the Norwegian Maritime Directorate and indicated in the trade certificate. The minimum freeboard shall be indicated by loading marks on the vessel’s sides in accordance with the standard marking form of the Norwegian Maritime Directorate.

§ 2-9
Ventilators

A new fourth paragraph should read:

(4)	In vessels constructed on 1 January 2003 or later, the height above deck of coamings of engine-room ventilators which are necessary for the continuous supply of air to the engine-room or immediate supply of air to the generator room shall be in accordance with the third paragraph. Where the size or design of the vessel makes such arrangement impractical, the Norwegian Maritime Directorate may approve a height reduction, provided that the ventilator is fitted with a weathertight closing appliance in accordance with the second paragraph, in combination with appropriate means for ensuring uninterrupted supply of air to the spaces concerned. Notwithstanding the above, the height shall be at least 900 mm above the working deck or superstructure deck.

§ 3-2
Stability criteria

The Section should read:

(1)	The following minimum stability criteria shall be met:

  - The area under the righting lever curve (GZ curve) shall not be less than 0.055 metre-radians up to 30 degrees angle of heel and not less than 0.090 metre-radians up to 40 degrees or the angle of flooding (f2 if this angle is less than 40 degrees. Additionally, the area under the curve between the angles of heel of 30 degrees and 40 degrees or between 30 degrees and (f if this angle is less than 40 degrees shall not be less than 0.030 metre-radians.

  - The righting lever GZ shall be at least 200 millimetres at an angle of heel equal to or greater than 30 degrees.

  - The maximum righting lever GZmax shall occur at an angle of heel preferably exceeding 30 degrees but not less than 25 degrees.

  - A vessel having a special hull design may, upon the approval of the Norwegian Maritime Directorate, comply with the minimum stability requirements set out in Appendix 4.

  - The initial metacentric height GM shall not be less than 350 millimetres.

  - The vessel’s metacentric height (GM) in the light condition shall be positive.

  - In vessels less than 24 metres in length (L), additionally the righting lever (GZ) for angles of heel between 40 and 65 degrees shall nowhere be less than 100 millimetres, and positive up to 80 degrees, not taking into account flooding through hatches, doors, bilge valves, etc. which must remain open during operation but which can rapidly be closed weathertight.

(2)	Where arrangements other than bilge keels are provided to limit the angles of roll, the stability criteria given in the first paragraph shall be maintained in all operating conditions.

(3)	Permanent ballast shall not be liquid or capable of being pumped. Ballast shall be so contained and secured that it cannot shift. Permanent ballast shall not be removed or moved from the vessel without the approval of the Norwegian Maritime Directorate.

### § 4-10
Arrangements for fuel oil, lubricating oil and other flammable oils

In the seventh paragraph, the last two sentences of subparagraph 1 should read:

Such flexible pipes and end attachments shall be of adequate strength and shall be constructed of approved fire-resistant materials or have fire-resistant coatings which comply with the requirements of the recognized classification society. In vessels constructed after 1 January 2003, end attachments shall be in accordance with the requirements set out in Appendix 4.

§ 5-2

Definitions

In the third paragraph, a new sentence is added at the end of subparagraph 5:

For vessels constructed after 1 January 2003, the Norwegian Maritime Directorate shall require that such a test be conducted.

In the fourth paragraph, a new sentence is added at the end of subparagraph 4:

For vessels constructed after 1 January 2003, the Norwegian Maritime Directorate shall require that such a test be conducted.

In the sixth paragraph, a new sentence is added at the end of subparagraph 3:

For vessels constructed after 1 January 2003, the Norwegian Maritime Directorate shall require that such a test be conducted.

§ 7-3

Evaluation, testing and approval of life-saving appliances and arrangements

In the second paragraph, subparagraph 3 should read:

3. 	for vessels constructed before 1 January 2003, have successfully undergone and passed tests which are substantially equivalent to the tests specified in Appendix 4.

Appendix 4

List og IMO resolutions, MSC/Circs., standards, Codes and conventions

Required by the present regulation

|  | Section | IMO Res. and MSC/Circ. | Conventions and Codes | Standards |
| --- | --- | --- | --- | --- |
| Chapter 3 Stability criteria | § 3-2 (1) sub. 4 | IMO Res. A 749 (18) para. 4.5.6.2.1 – 4.5.6.2.4 |  |  |
| Chapter 4 Arrangements for fuel oil, lubricating oil and other flammable oils | § 4-10 (7) sub. 1 | MSC/Circ.647 |  |  |