#### NORWEGIAN RADIO INTERFACE

NRI-0041

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES - WIRELESS MICROPHONES

FOR PEOPLE WITH HEARING IMPAIRMENTS

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 173.8125 MHz 173.8375 MHz 173.9125 MHz 173.9375 MHz 173.9625 MHz | The numbers refer to center frequencies. |
| Power level | Max. 1.0 mW e.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | Max. 25 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 422-2 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0042

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES -

REMOTE CONTROLS FOR MODEL CARS AND MODEL BOATS

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 35.310 - 35.390 MHz | Numbers refer to center frequencies, which are separated by 10 kHz, i.e. center frequencies are located at: 35.310, 35.320, 35.330, 35.340 MHz etc. |
| Power level | Max. 100 mW e.r.p. |  |
| Channel separation | 10 kHz |  |
| Bandwidth | Max. 10 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 220-3 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0043

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES -

REMOTE CONTROLS FOR MODEL CARS AND MODEL BOATS

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 40.705 - 40.795 MHz | Numbers refer to center frequencies, which are separated by 10 kHz, i.e. center frequencies are located at: 40.705, 40.715, 40.725, 40.735 MHz etc. |
| Power level | Max. 100 mW e.r.p. |  |
| Channel separation | 10 kHz |  |
| Bandwidth | Max. 10 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 220-3 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0044

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES - REMOTE CONTROL OF CRANES

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 440.725 MHz 440.750 MHz 441.325 MHz 441.550 MHz 441.575 MHz 441.600 MHz 441.625 MHz 441.725 MHz | Numbers refer to center frequencies. |
| Power level | Max. 100 mW e.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | Max. 25 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 220-3 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0045

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES - MEDICAL TELEMETRY

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 441.750 - 441.975 MHz | Numbers refer to center frequencies, which are separated by 25 kHz, i.e. center frequencies are located at: 441.750, 441.775, 441.800, 441.825 MHz etc. |
| Power level | Max. 10 mW e.r.p. |  |
| Channel separation | 25 kHz |  |
| Bandwidth | Max. 25 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 220-3 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0046

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES -

5 GHZ RLAN

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 5470 - 5725 MHz |  |
| Power level | Max. 1 W e.i.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | draft EN 301 893 |  |
| Type of licence | General licence | This does not apply to devices or installations on the Norwegian part of the continental shelf. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0047

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES - HOMING EQUIPMENT

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 2275 Hz |  |
| Power level | Max. 42 dBμA/m at 10 m |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 718-2 |  |
| Type of licence | General licence | This does not apply to devices or installations on the Norwegian part of the continental shelf. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | EN 300 718-3 |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0048

(Issue 16.10.2002)

SHORT RANGE DEVICES - HOMING EQUIPMENT

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 457 kHz |  |
| Power level | Max. 7 dBμA/m at 10 m |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 718-2 |  |
| Type of licence | General licence | This does not apply to devices or installations on the Norwegian part of the continental shelf. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | EN 300 718-3 |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0049

(Draft issue 16.10.2002)

SHORT RANGE DEVICES - HOMING EQUIPMENT

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 142.275 MHz 142.325 MHz | Numbers refer to center frequencies. |
| Power level | Max. 500 mW e.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | 25 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 220-3 |  |
| Type of licence | General licence | This does not apply to devices or installations on the Norwegian part of the continental shelf. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0050

(Draft Issue 16.10.2002)

CORDLESS TELEPHONES CT1

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 914 - 915 MHz 959 - 960 MHz | Portable Part Fixed Part |
| Power level | Max. 10 mW e.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | 25 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 301 796 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0051

(Draft Issue 16.10.2002)

CORDLESS TELEPHONES - DECT

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 1880 - 1900 MHz |  |
| Power level | Max. 250 mW e.i.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 301 406 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0052

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 61.0 - 61.5 GHz |  |
| Power level | Max. 100 mW e.i.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | Not specified |  |
| Type of licence | General licence | This does not apply to devices or installations on the Norwegian part of the continental shelf. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0053

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 122 - 123 GHz |  |
| Power level | Max.100 mW e.i.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | Not specified |  |
| Type of licence | General licence | This does not apply to devices or installations on the Norwegian part of the continental shelf. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0054

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 244 - 246 GHz |  |
| Power level | Max.100 mW e.i.r.p. |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | Not specified |  |
| Type of licence | General licence | This does not apply to devices or installations on the Norwegian part of the continental shelf. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0055

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES - RAILWAY EUROLOOP

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 4515 kHz |  |
| Power level | Max. 7 dBμA/m at 10 m (ref. CEPT/ERC/REC 70-03 Annex 4, Figure 2) | Transmitting only on receipt of a Eurobalise telepowering signal from a train. |
| Channel separation | Not specified |  |
| Bandwidth | Ref. CEPT/ERC/REC 70-03 Annex 4, Figure 2 |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 330-2 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0056

(Draft Issue 16.10.2002)

SHORT RANGE DEVICES - INDUCTIVE APPLICATIONS

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 7.4 – 8.8 MHz |  |
| Power level | Max. 9 dBμA/m at 10 m |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 330-2 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0057

(Draft Issue 16.10.2002)

PRIVAT RADIO - PR 27

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency bands | 26.965 - 26.985 MHz 27.005 - 27.035 MHz 27.055 - 27.085 MHz 27.105 - 27.135 MHz 27.155 - 27.185 MHz 27.205 - 27.405 MHz | Numbers refer to center frequencies, which are separated by 10 kHz in each group, i.e. center frequencies are located at: 26.965, 26.975, 26.985, 27.005, 27.015, 27.025, 27.035, 27.055 MHz etc. (as in EN 300 135) |
| Power level | Max. 4.0 W e.r.p. |  |
| Channel separation | 10 kHz |  |
| Bandwidth | 10 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 300 135-2 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0058

(Draft Issue 16.10.2002)

SATELLITE TERMINAL EQUIPMENT - SIT

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 10.70 - 12.75 GHz 29.50 - 30.00 GHz | Downlink Uplink |
| Power level | Max. 2 W Max. 50 dBW e.i.r.p. | Antenna diameter is up to 1.2 m |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 301 459 |  |
| Type of licence | General licence | This provision does not apply to Svalbard or inside the perimeter fence of an airfield and 500 meters beyond |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0059

(Draft Issue 16.10.2002)

SATELLITE TERMINAL EQUIPMENT - SUT

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 19.70 - 20.20 GHz 29.50 - 30.00 GHz | Downlink Uplink |
| Power level | Max. 2 W Max. 50 dBW e.i.r.p. | Antenna diameter is up to 1.8 m |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 301 459 |  |
| Type of licence | General licence | This provision does not apply to Svalbard or inside the perimeter fence of an airfield and 500 meters beyond. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0060

(Draft Issue 16.10.2002)

SATELLITE TERMINAL EQUIPMENT - VSAT

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 10.7 - 11.7 GHz 12.5 - 12.75 GHz 14.0 - 14.5 GHz | Downlink Downlink Uplink |
| Power level | Max. 2 W Max. 50 dBW e.i.r.p. | Antenna diameter is up to 3.8 m. |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 301 428 |  |
| Type of licence | General licence | This provision does not apply to Svalbard or inside the perimeter fence of an airfield and 500 meters beyond. |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0061

(Draft Issue 16.10.2002)

SATELLITE TERMINAL EQUIPMENT - ARGOS

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 401.650 +/- 0.005 MHz |  |
| Power level | Not specified |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | Not specified |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0062

(Draft Issue 16.10.2002)

SATELLITE TERMINAL EQUIPMENT - INMARSAT B, M, M4 and MINI-M

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 1525 - 1559 MHz 1626.5 - 1660.5 MHz | Downlink (except 1544 - 1545 MHz) Uplink (except 1645.5 - 1646.5 MHz) |
| Power level | Not specified |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 301 444 |  |
| Type of licence | General licence | This provision does not apply to maritime and aeromobile Inmarsat terminals |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0063

(Draft Issue 16.10.2002)

SATELLITE TERMINAL EQUIPMENT -

OMNITRACS TERMINALS FOR THE EUTELTRACS SYSTEM

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 10.7 - 11.7 GHz 12.50 - 12.75 GHz 14.00 - 14.25 GHz | Downlink Downlink Uplink |
| Power level | Not specified |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 301 427 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0064

(Draft Issue 16.10.2002)

SATELLITE TELEPHONES - GLOBALSTAR

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 1610.00 - 1621.35 MHz |  |
| Power level | Not specified |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | Not specified |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0065

(Draft Issue 16.10.2002)

SATELLITE TERMINAL EQUIPMENT - INMARSAT C and D

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 1525 - 1559 MHz 1626.5 - 1660.5 MHz | Downlink (except 1544 - 1545 MHz) Uplink (except 1645.5 - 1646.5 MHz) |
| Power level | Not specified |  |
| Channel separation | Not specified |  |
| Bandwidth | Not specified |  |
| Duty cycle | Not specified |  |
| Type of transmission | Not specified |  |
| Technical Standard 1) | EN 301 426 |  |
| Type of licence | General licence | This provision does not apply to maritime and aeromobile Inmarsat terminals |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.: