NORWEGIAN RADIO INTERFACE

NRI-0067

(Draft Issue 09.12.2002)

PROFESSIONAL MOBILE RADIO (PMR) ANALOG SYSTEMS (VHF)

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band ” ” ” ” ” ” ” ” | 68.000 - 74.800 MHz 75.200 - 87.500 MHz 138.000 - 140.500 MHz 142.500 - 144.000 MHz 146.000 - 147.500 MHz 149.500 - 152.000 MHz 154.000 - 156.000 MHz 158.000 - 160.600 MHz 162.025 - 174.000 MHz | Simplex and duplex bands ” ” ” ” ” ” ” ” |
| Power level (max.) | 25 W e.r.p. (base station) | 15 W e.r.p. (mobile stations) 5 W e.r.p. (handheld stations) |
| Channel separation | 25 kHz |  |
| Bandwidth | 16 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | F3EJN G3EJN F3DJN |  |
| Technical Standard 1) | EN 300 086-2, EN 300 113-2, EN 300 296-2, EN 300 219-2, EN 300 341-2, EN 300 390-2 |  |
| Type of licence | Individual |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0068

(Draft Issue 09.12.2002)

PROFESSIONAL MOBILE RADIO (PMR) ANALOG SYSTEMS (UHF)

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band ” ” ” ” ” ” ” ” ” ” | 406.100 - 410.000 MHz 415.425 - 420.000 MHz 425.425 - 426.800 MHz 438.800 - 439.000 MHz 439.600 - 440.000 MHz 442.750 - 445.000 MHz 445.800 - 446.000 MHz 446.600 - 447.000 MHz 447.750 - 453.000 MHz 457.500 - 463.000 MHz 467.500 - 470.000 MHz | Simplex and duplex bands ” ” ” ” ” ” ” ” ” ” |
| Power level (max.) | 25 W e.r.p. (base station) | 15 W e.r.p. (mobile stations) 5 W e.r.p. (handheld stations) |
| Channel separation | 25 kHz |  |
| Bandwidth | 16 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | F3EJN G3EJN F3DJN |  |
| Technical Standard 1) | EN 300 086-2, EN 300 113-2, EN 300 296-2, EN 300 219-2, EN 300 341-2, EN 300 390-2 |  |
| Type of licence | Individual |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.:

NORWEGIAN RADIO INTERFACE

NRI-0069

(Draft Issue 09.12.2002)

SHORT DISTANCE RADIO “KDR 444”

| Interface parameters | Description | Comments |
| --- | --- | --- |
| Frequency band | 444.600 MHz, 444.650 MHz, 444.800 MHz, 444.825 MHz, 444.850 MHz, 444.975 MHz | Numbers refer to center frequencies. |
| Power level | Max. 0.5 W e.r.p. |  |
| Channel separation | 25 kHz |  |
| Bandwidth | 16 kHz |  |
| Duty cycle | Not specified |  |
| Type of transmission | F3EJN G3EJN F3DJN |  |
| Technical Standard 1) | EN 300 296-2 |  |
| Type of licence | General licence |  |
| Essential requirements (As defined in Directive 1999/5/EC, article 3.3) | Not specified |  |

1) Norwegian Post and Telecommunications Authority proposes that the above mentioned equipment should comply with the requirements of this

ETSI standard to the extent that they relate to the essential requirements of Directive 1999/5/EC.

This interface has been notified to the European Commission according to Directive 1999/5/EC, article 4, based on the provisions of

Directive 98/34/EC, under notification no.: