# Draft regulation june 2001

# Regulation on hooks for transport in slaughterhouses

(Issued by Norwegian Metrology and Accreditation Service on xx.xx.2001 pursuant to Section 22, 23 and 50 of Act No 2 relating to Weights and Measures and Regulation on Verification of 24. August 1999, section 11)

§ 1 (field of activity)

This regulation applies to hooks used for transport during the production process in slaughterhouses, were the hook is weighed together with the product and the hook is considered to have a constant mass.

§ 2 (verification)

Hooks according to § 1 shall always be verified if the mass of the hook is set as a constant tare.

§ 3 (verification tolerance)

The maximum permissible error is given as:

mpe = K + 20 were mpe is in g when K (nominal mass) is given in kg.

§ 4 (general regulations)

The hooks referred to in § 1 can be verified without any type approval.

If part of the hook can be removed and the hook still may be used for transport, then these parts shall be secured mechanically to the hook.

§ 5 (security and descriptive markings)

Each hook shall be marked with nominal mass; verification mark shall be stamped on the hook close to the marking of the nominal mass.

§ 6 (entry into force)

This regulation enters into force on 1st of January 2002.