Draft

Regulation xx.xx 2005 concerning amendment of Regulation of 11 October 2004 concerning life-saving appliances on passenger ships

Laid down by the Norwegian Maritime Directorate on xx.xx 2005 pursuant to the Act of 9 June 1903 No. 7 relating to Public Control of the Seaworthiness of Ships, etc., § 1, § 41a, § 42, § 47, § 48, § 97, and § 100, ref. Royal Decrees of 5 April 1963 No. 9 and 1 December 1978 No. 12.

I

Section 1 shall be replaced by the following:

§ 1

Scope of application

(1)	This Regulation applies to passenger ships which are certified to carry more than 12 passengers, as follows:

a)	All passenger ships irrespective of size operating in trade area 2 or a lesser trade area.

b)	Passenger ships which are built prior to 1 May 2000, of less than 24 metres in length (L) operating in trade areas 3, 4 and small coasting.

c)	For passenger ships of 24 metres and upwards in length (L) which are built prior to 1 May 2000 and to which the Regulation of 28 March 2000 No. 305 concerning surveys, construction and equipment of passenger ships engaged on domestic voyages applies, the requirements of this Regulation shall apply until the date of upgrading as provided in the Regulation of 28 March 2000 No. 305, Section 8 third paragraph, subparagraph d.

(2)	Passenger ships engaged on international voyages, and passenger ships holding international certificates engaged on domestic voyages, which are certified to carry more than 12 passengers shall comply with all requirements currently in force relating to life-saving equipment contained in Chapter III of the 1974 SOLAS Convention. Additionally, Sections 1 to 6, 20, 35 and 36 of this Regulation shall apply.

(3)	With the exception of Sections 1 to 6, 8, 9 first paragraph,10, 34, 35 and 36, this Regulation does not apply to passenger ships which are certified to carry 12 or fewer passengers.

(4)	This Regulation does not apply to ships covered by Directive 98/18/EC on safety rules and standards for passenger ships.

Section 2 shall be replaced by the following:

§ 2

Definitions

(1)	For the purpose of this Regulation:

a)	Recognized classification society means classification societies with which the Ministry has entered into an agreement pursuant to § 9 of the Seaworthiness Act:

1. 	Det Norske Veritas (DNV)

2. 	Lloyd’s Register of Shipping (LRS).

3.	Bureau Veritas (BV).

4. 	Germanischer Lloyd (GL).

5. 	American Bureau of Shipping (ABS).

b)	Accepted means equipment accepted by the Norwegian Maritime Directorate on the basis of approval or type-approval by a recognized classification society, another public or private institution, or the administration of a country which has ratified the SOLAS Convention.

c)	Anti-exposure suit means a protective suit designed for use by crews in rescue boats and crews operating MES.

d)	Gross tonnage means the numerical value for gross tonnage entered in the Tonnage Certificate. If safety tonnage is entered in the ”Remarks” column of the Tonnage Certificate, the numerical value for such tonnage shall apply as gross tonnage.

e)	Built means:

1. 	the ship is at a stage of construction where the keel is laid; or

2. 	construction identifiable with a specific ships begins; or

3. 	assembly of that ship has commenced comprising at least 50 tonnes or 1 % of the estimated mass of all structural material, whichever is less.

f)	IMO means the International Maritime Organization.

g)	Length (L) means, unless otherwise excplicitly provided for in the provisions of each Section of this Regulation, 96 % of the total length on a waterline at 85 % of the least moulded depth measured from the top of the keel, or the length from the fore side of the stem to the axis of the rudder stock on that waterline, whichever is the greater. In ships designed with a rake of keel, the waterline on which this length is measured shall be parallel to the designed waterline.

h)	LSA Code means the International Life-Saving Appliance Code, adopted by the Maritime Safety Committee of the IMO by resolution MSC.48(66), as amended by the IMO.

i)	Passenger ship means a ship which pursuant to the provisions in Chapter VIII of the Act of 9 June 1903 No. 7 relating to Public Control of the Seaworthiness of Ships, etc. is required to hold a passenger certificate or a passenger ship safety certificate.

j)	Immersion suit means a protective suit which reduces loss of body heat for a person immersed in cold water. May be insulated or uninsulated.

k)	Survival craft means a lifeboat, rescue boat and liferaft.

l)	Seasonal craft means a passenger ship which is not a high-speed craft, of less than 300 gross tonnage, operating in trade area 1 and lesser trade area within the time period 1 May to 30 September.

m)	SOLAS Convention means the International Convention for the Safety of Life at Sea, 1974, as amended by the IMO.

n)	Thermal suit means a suit that offers thermal protection, and which reduces loss of body heat for a person immersed in cold water. To be used together with a lifejacket.

o)	Thermal lifejacket means a lifejacket that offers thermal protection and which reduces loss of body heat for a person immersed in cold water.

(2)	Otherwise, the definitions in regulation III/3 of the SOLAS Convention shall apply.

Section 7 shall be replaced by the following:

§ 7

Life-saving appliances

Any ship shall, according to its date of construction, trade area and number of passengers, carry at least the life-saving appliances which are specified in the below table.

| Trade area Equipment | All ships in trade area 2 or a lesser trade area | Ships built prior to 1 May 2000 in trade areas 3 and 4 and small coasting, of length (L) ≥ 24 m | Ships built prior to 1 May 2000 in trade areas 3 and 4 and small coasting, of (L) < 24 m | § |
| --- | --- | --- | --- | --- |
| Number of persons on board (N) | <250 ≥250 | <250 ≥250 |  |  |
| Survival craft | 1.1 N | 1.1N | 1.1N | § 9 |
| Rescue boats | 1 | 1 | 1 | § 13 |
| Marine Evacuation Systems (MES) | Cf. § 15 | Cf. § 15 | Cf. § 15 | § 15 |
| Lifebuoys: ships of an overall length: ≥ 15m < 15 m | 4 8 2 | 4 8 | 4 2 | § 18 |
| Lifejackets/thermal lifejackets/thermal suits in combination with lifejackets | 1.05N | 1.05N | 1.05N | § 20 |
| Lifejackets/thermal lifejackets for children | 0.1N | 0.1N | 0.1N | § 20 |
| Immersion suit / anti-exposure suits | Cf. § 21 | Cf. § 21 | Cf. § 21 | § 21 |
| Rocket parachute flares | 3 | 12 | 12 | § 19 |
| Line-throwing appliance * | 0 | yes | yes | § 19 |
| Radar transponder ** | 1 | 1 | 1 | § 19 |
| Two-way, portable VHF radiotelephone apparatus *** | 2 3 | 2 3 | 2 | § 19 |

* The requirement for a line-throwing appliance applies to trade area 4 and small coasting

** The requirement for a radio transponder applies to trade area 2 and greater trade areas

*** The requirement for a portable VHF applies to trade area 1 and greater trade areas

Section 8 shall be replaced by the following:

§ 8

Life-saving appliances on board ships certified to carry 12 or fewer passengers

Ships certified to carry 12 or fewer passengers shall be provided with the following life-saving appliances, as a minimum:

a)	Liferaft(s) capable of accommodating all persons on board, cf. Section 9, first paragraph;

b)	lifejackets/thermal lifejackets/thermal suits in combination with lifejakets, pursuant to Section 20 for all persons on board;

c)	one lifebuoy fitted with a light and a buoyant lifeline;

d) 	three rocket parachute flares;

e) 	an appliance that makes it possible to recover a person from the water;

f)	for open boats operating on lakes and rivers, thermal lifejackets/thermal suits in combination with lifejackets for all persons on board and one lifebuoy fitted with a light and a buoyant lifeline shall be permitted as the sole life-saving appliances carried. This provides the presence of an appliance that makes it possible to recover a person from the water.

Section 9 shall be replaced by the following:

§ 9

Survival craft

(1)	For trade area 3 and lesser trade areas, the Norwegian Maritime Directorate may accept open reversible inflatable liferafts complying with the requirements of Annex 11 to the High-Speed Craft (HSC) Code, 2000.

(2)	Survival craft shall, as far as practicable, be evenly distributed on both sides of the ship. For ships built prior to 1 July 2005, the requirement for an increase from 100 % to 110 % (1.1 N) shall apply no later than the date of the first certificate survey following 1 January 2006.

(3)	The number of survival craft carried shall be sufficient to ensure that in the case of loss or unusability of any one survival craft, the remaining survival craft may accommodate the total number of persons which the ship is certified to carry. For ships built prior to 1 July 2005, the requirement shall apply no later than the date of the first certificate survey following 1 January 2006.

(4)	No lifeboat or rescue boat shall be required to marshal more than nine liferafts.

Section 13 shall be replaced by the following:

§ 13

Rescue boats

(1)	Rescue boats shall be provided with separate launching arrangements capable of both launching and recovery. For ships built prior to 1 July 2005, the requirement shall apply no later than the date of the first certificate survey following 1 January 2006.

(2)	The rescue boat may be included in the survival craft capacity.

(3)	The rescue boat shall be fitted with a rescue frame for recovery of persons from the sea.

(4)	For ships of less than 24 m in length (L), an exemption from the requirement for a rescue boat may be granted, provided that the following conditions are met:

a) 	the ship is provided with devices enabling the recovery of a helpless person from the water;

b)	the recovery of a helpless person may be observed from the bridge; and

c)	the ship’s manoeuvrability is such that it may go close to and recover persons in all conditions.

(5)	Ships in trade area 1 and lesser trade areas may as an alternative to launching arrangements keep a rescue boat under tow, provided that the ship is fitted with means of access for embarkment onto a rescue boat.

Section 14 shall be replaced by the following:

§ 14

Rescue boat embarkation and launching arrangements

(1)	Rescue boat embarkation and launching arrangements shall be such that the embarkation and launching operation may be performed in the shortest possible time. Altogether, embarkation and launching shall not take more than five minutes.

(2)	The rescue boat shall be capable of being embarked and launched directly from the stowed position carrying the number of persons designated as the rescue boat crew.

(3)	Rescue boats shall be capable of being launched as the vessel moves ahead at a speed of up to five knots.

Section 15 shall be replaced by the following:

§ 15

Marine evacuation systems (MES)

(1)	Ships in which the distance from the waterline to the embarkation deck is 1.5 metres or more in any intact or damaged condition whatsoever pursuant to approved stability calculations, shall be provided with type-approved marine evacuation systems (MES) or a similar equivalent arrangement that enables passengers to embark the life-saving appliances in a safe manner. For ships that are not subject to stability calculations requirements, the distance from the waterline to the embarkation deck shall be measured in lightship condition.

(2)	The marine evacuation systems or arrangements shall, as far as practicable, be evenly distributed on both sides of the ship. For ships built prior to 1 July 2005, the requirement shall apply no later than the date of the first certificate survey following 1 January 2006.

(3)	For ships where the distance from the waterlines mentioned in the first paragraph to the embarkation deck is less than 1.5 metres, the Norwegian Maritime Directorate may accept that passengers embark the liferafts directly. The liferafts shall be capable of being moored to the embarkation station in a secure manner

(4)	The provisions in Chapter 6 of the LSA Code shall be complied with.

Section 17 shall be replaced by the following:

§ 17

Embarkation stations and embarkation arrangements

The embarkation stations and embarkation arrangements shall be fitted in such a way as to remain operational at an angle of heel of 10° to any side. Alternatively, the ship shall have at least one embarkation station with appurtenant arrangements on each side, with a capacity of at least 100 % of the number of passengers.

Section 18 shall be replaced by the following:

§ 18

Lifebuoys

(1)	At least one of the lifebuoys on either side shall be fitted with a buoyant lifeline which is at least 30 metres long.

(2)	At least one of the lifebuoys on either side shall be fitted with a self-igniting smoke signal and a self-igniting light, however without a buoyant lifeline. They shall be capable of quick release from the bridge.

(3)	Other lifebuoys on board shall be fitted with a self-igniting light, however without a buoyant lifeline.

(4)	On ships for which only two lifebuoys are required, one of the lifebuoys shall be fitted with a buoyant lifeline which is at least 30 metres long, while the other shall be fitted with a self-igniting light, however without a buoyant lifeline.

Section 19 shall be replaced by the following:

§ 19

Rocket parachute flares/line-throwing appliance/

radar transponder/two-way, portable VHF radiotelephone apparatus

Rocket parachute flares, line-throwing appliance, radar transponder and two-way, portable  VHF apparatus shall be located in a readily accessible place on the bridge.

Section 21 shall be replaced by the following:

§ 21

Immersion suits and anti-exposure suits

(1)	All crew members, including catering personnel, who will be piloting survival craft or manning marine evacuation systems, shall be provided with an immersion suit or an anti-exposure suit. For ships built prior to 1 July 2005, the requirement shall apply no later than the date of the first certificate survey following 1 January 2006.

(2)	The suit shall be of a type which is fitted with detachable gloves or gloves that do not prevent the crew member performing necessary duties and operating necessary equipment in an emergency.

Section 22 shall be replaced by the following:

§ 22

Escape routes, muster stations and illumination

(1)	Escape routes, muster stations and embarkation stations shall be illuminated by light sources powered by the main source of electrical power and by the emergency source of electrical power.

(2)	For ships built on or following 1 July 2005, the muster stations and the appurtenant embarkation stations, including escape routes between them, shall be separated in a manner that ensures proper fire-prevention from open car decks by a class A-30 division.

a)	If the ship has muster capacity and survival craft for at least 100 % of the number of passengers on each side, at least half of this capacity shall be separated in a manner that ensures proper fire-prevention from open car decks by a class A-30 division.

(3)	For ships built on or following 1 July 2005, escape routes shall have a capacity that allows a safe escape. The muster stations shall have an unobstructed deck space of 0.35m2 per person as a minimum, unobstructed deck space may include floor space used for seating. The muster stations shall be designed in such a way as to allow the effective control of passengers, and be located in connection with places where passengers embark onto survival craft. If a muster station cannot be located in the immediate proximity of an embarkation station, the escape route between them shall have the capacity to allow a safe escape.

Section 25 shall be replaced by the following:

§ 25

General alarm system

(1)	All ships shall be provided with a general alarm system.

(2)	The general alarm system shall comply with the requirements of Chapter 7 of the LSA Code.

(3)	For ships built prior to 1 July 2005, the requirements of the first and second paragraphs shall apply no later than the date of the first certificate survey following 1 January 2006.

(4)	For ships engaged on domestic voyages of less than 24 metres in length (L) an alarm signal given with the ship’s whistle or siren may be accepted as an alternative to the general alarm system.

(5)	The general alarm system shall be capable of summoning passengers and crews to the muster stations and initiate the operations indicated in the muster list.

(6)	Seasonal craft may be exempted from the requirement for a general alarm system if the crew and the passengers may be alerted directly from the bridge.

Section 26 shall be replaced by the following:

§ 26

Public address system (PA system)

(1) 	All ships certified to carry more than 36 passengers shall be provided with a PA system.

(2)	The PA system shall comply with the requirements of Chapter 7 of the LSA Code.

(3)	For ships built prior to 1 July 2005, the requirements of the first and second paragraphs shall apply no later than on the date of the first certificate survey following 1 January 2006.

(4)	The PA system shall be fitted with an overriding function which is operated from one location on the bridge and from such other locations on board as are determined by the Norwegian Maritime Directorate. The overriding function shall ensure that all messages in an emergency may be broadcast in the event that a loudspeaker in any particular space is turned off, the volume of the loudspeaker is turned down, or the PA system is being used for other purposes.

(5)	PA systems on board ships which are built on or after 1 July 2005 shall comply with the following requirements:

a)	The system shall have at least two circuits, well separated, and at least two separate and independent amplifiers. Recommendations of the IMO currently in force shall be taken into account.

b)	The PA system shall be powered by the main source of electrical power and by the emergency source of electrical power.

(6)	Seasonal craft may be exempted from the requirement for a public address system, if the crew and passengers may be alerted directly from the bridge.

Section 27 shall be replaced by the following:

§ 27

Muster list

(1)		A muster list shall be prepared for all ships.

(2)		The muster list shall be posted in conspicuous places on board, including the bridge, the engine-room and the crew accommodation.

(3)		The muster list shall be readable in emergency lighting.

(4)		The muster list shall be in the Norwegian language.

(5)		The muster list shall provide detailed information about the general emergency alarm and the PA system and indicate the action to be taken by the crew and the passengers when the general emergency alarm is sounded. Additionally, it shall indicate how the abandon ship order will be given.

(6)		The duties of the different crew members in an emergency shall appear from the muster list and shall include:

a)	closing of watertight doors, fire doors, valves, freeing ports, hatches, skylights, side scuttles and other similar openings in the ship;

b)	equipment of survival craft and other life-saving appliances;

c)	preparation and launching of survival craft;

d)	general preparation of other life-saving appliances;

e)	mustering of passengers;

f)	use of communication equipment;

g)	setting up of a fire team to fight a fire; and

h)	special duties related to the use of fire-fighting equipment and installations.

(7)		The muster list shall identify the officers responsible for ensuring that life-saving and fire-fighting equipment is kept in good working order and is ready for immediate use.

(8)		Replacements for key personnel shall be identified in the muster list, regard being had to the need for different action to be taken in different emergencies.

(9)		The muster list shall indicate the emergency duties to be performed by the crew members in relation to the passengers. Such duties shall include:

a)	alerting the passengers;

b)	ensuring that the passengers wear suitable clothing and have donned their lifejackets correctly;

c)	assembling the passengers at the muster stations; and

d)	keeping order in corridors and stairways and generally supervising and controlling the movements of the passengers.

(10)	Every ship shall have procedures for the location and rescue of passengers who are trapped inside their cabins.

(11)	The muster list of a passenger ship which is certified to carry more than 300 passengers shall be approved by the Norwegian Maritime Directorate.

Section 34 shall be replaced by the following:

§ 34

Control and maintenance

(1)	As long as the ship is operative, all life-saving appliances shall comply with applicable regulations and shall be ready for immediate use.

(2)	The control of life-saving appliances shall comply with the guidance currently in force issued by the Norwegian Maritime Directorate.

(3)	Instructions on maintenance shall comply with the provisions of Chapter III of the SOLAS Convention and shall be carried on board.

(4)	The provisions of Chapter III of the SOLAS Convention on the maintenance of life-saving equipment shall apply.

(5)	Maintenance shall be carried out by qualified and certified personnel in compliance with Chapter III of the SOLAS Convention.

(6)	Equipment shall as far as possible be function-tested following maintenance.

(7)	All maintenance must be possible to document.

II

This Regulation enters into force 1 July 2005.

# Footnotes

IMO Resolution A.686(17)/MSC/Circ.810