NOTIFICATION

Notification on the EFTA-EU procedure according to Directive 98/34/EC

1.        Special code.

2.        State:  Iceland (IS)

3.A        Ministry for Foreign Affairs

Rauðararstigur 25

IS-150 Reykjavík

Iceland

Tel +(354) 560 9900 Fax +(354) 562 4878

3.B        Origination Ministry or Authority:

Civil Aviation Administration

Flugturninum Reykjavíkurflugvelli

IS-101 Reykjavík
Iceland

Tel +(354) 569 4100 Fax +(354) 562 3619

4.      Notification:  2005/9009/IS

5.      Title:  Regulation on microlights

6.      Products concerned:   Microlights

7.      Notification under Community Act:  Directive 98/34/EC of the European Parliament and of the Council laying down a procedure for the provision of information in the field of technical standards and regulations.

8.      Main content:  There are no international standards for microlights. The Icelandic regulation is applicable to all microlights flying in Iceland within Icelandic national airspace and sets the parameters that define a microlight and where and who may operate one, rules concerning registration, minimum equipment and maintenance etc.

The Icelandic regulation defines microlight as an aircraft that has no more than two seats and a maximum VSO speed in landing configuration of 35 knots (65 km/h) indicated CAS and a maximum take-off mass no more than: 300 kg for a land Microlight (landplane) with one seat, or 450 kg for a land microlight with two seats, or 330 kg for an amphibian microlight or a microlight with floats (floatplane) with one seat, or 495 kg for an amphibian microlight or a microlight with floats with two seats, provided that the microlight can be used both as a microlight with floats and a land microlight such that it is within the limits of both categories with regard to maximum take-off mass, as applicable. An aircraft without an engine, lighter than 70 kg is categorised as a microlight without an engine. An engine driven aircraft, lighter than 70 kg and take-off is by foot is categorised as a microlight without an engine. Parachutes are not categorised as microlights.

The Icelandic regulation limits the use of Microlights to recreation or sports. It is prohibited to fly a microlight for commercial purposes, for transport or aerial work, or for other work except instruction and training and examining.

9.      Brief statement of grounds:  There are no international standards for Microlights but it is considered necessary to set up a harmonised safety regime for the operation and definition of such “aircraft”.

10.     Reference documents:  The based on earlier Icelandic Regulations and similar regulations set by other States taking into account specific Icelandic operational environment.

11.        Invocation of the Emergency Procedure:  No.

12.        Grounds for the emergency:   No

13.        Confidentiality:  No.

14.        Fiscal Measures:  No.