”Amendments to the Norwegian Motor Vehicle Construction Regulation.

Laid down by the Directorate of Public roads dd.mm.yyyy with legal authority in the Road Traffic Act 18 June 1965 no. 4 Sections 13, 14, 15 and 16, cf. Delegation Decision from the Ministry of Transport and Communications of 24 November 1980.

I

In Regulation 4 October 1994 no. 918 concerning Motor Vehicle Construction the following amendments will be made:

Art. 28-1, no. 4-9 to 4-12 shall read:

4.9. The Regulations in Section 28-1 Nos. 2 and 3, apply to main beams, with the following additions:

Number of: Up to 4 additional, i.e. 6 in total for N3 vehicles.

Requirements regarding brightness: maximum brightness for all lamps for main beam which may

be on simultaneously (permitted with a switch), must not exceed 480 lux.

Other requirements: as laid down in Directive/Standards as given in Section 28-1, Nos. 2 and 3.

4.10. High Mounted Marker Lamps

1. At the front of a vehicle having a width of 1.80 m or more, up to 2 additional high mounted

marker lamps (i.e. 4 in all) are permitted in addition to the requirements in Section 28-1,

Nos. 2 and 3. These must be distributed with up to two on the cab and/or two on any builtup

body. The lamps must be positioned as stated in the Directives/Standards mentioned in

Section 28-1, Nos. 2 and 3.

2. On vehicles having a width of 2.10 m or more, 3 high mounted marker lamps are allowed, in

addition to the lamps mentioned in No. 1.

Position:

In Width: Symmetrically to the longitudinal centreline of the vehicle.

In Height: As given in the Directives/Standards mentioned in Section 28-1, Nos. 2 and 3.

In Length: At the front, on the upper limit of the cab. The horizontal plane which is tangent to the upper edge of the light emitting surface of the lamp must not be lower than the horizontal plane

tangent to the upper edge of the transparent zone of the windscreen.

4.11. The Regulations in the Directives/Standards mentioned in Section 28-1, Nos. 2 and 3 apply to side marker lamps. But vehicles with a width of 1.80 m or more may in addition have 2 lamps on each side of the vehicle. These lamps must be of the type combined high mounted marker lamps, emitting a white light to the front, and a red light to the rear. Requirements regarding position height: as for side marker lamps; length no more than1 000 mm from the front most and rearmost edge/limitation respectively of the cargo carrier (or goods/passenger compartment). The distance in respect of the lamps fitted on the front limitation, may possibly be increased so that the lamps can be seen from the driving seat through the external rear-view mirrors of the vehicle. The distance to other lamps must be at least 200 mm. The distance from the vehicles outer side-plane and out to the light emitting surface of the lamp may in addition be max. 50 mm if it is mounted on a rubber arm or similar, flexing when subjected to a force of 2 kp, applied in the centre of the lamp, and so that the direction of the force follows the horizontal plane in the vehicles longitudinal direction.

Trailers may have lamps as mentioned above, on both sides, front and rear. The mounting

requirements are the same as for vehicles.

4.12 The Regulations in Section 28-1, Nos. 2 and 3, apply to marker lamps (rear lamps) on vehicles and trailers, with the following additions:

Number of: Up to 10 extra (i.e. 12 in total), distributed with up to 6 down and 6 up.

Position

In Width: As laid down in the Directives/Standards mentioned in Section 28-1, Nos. 2 and 3.

For lamps fitted low down the height above the ground must be: Not less than 350 mm, and not

more than 1 500 mm, or not more than 2 100 mm if the shape of the body makes it impossible to

keep within the limit of 1 500 mm (as given in the Directive). For lamps fitted higher up, the

distance from the uppermost edge of the lamp's light emitting surface must not be more than

400 mm from the horizontal pane tangent to the upper, rearmost edge.

In Length: As laid down in the Directives/Standards mentioned in Section 28-1, Nos. 2 and 3.

Alternative Standards: Lamps approved and marked according to the SAE or DOT Standard shall be accepted, provided that the colour is more or less in accordance with the Directives/Standards mentioned in Section 28-2, Nos. 2 and 3.

Art. 28-1, no. 4-14 shall read:

4.14 The Regulations in Section 28-1, Nos. 2 and 3, apply to direction indicators on the rear of vehicles and trailers, with the following additions:

Number of: 2 additional ones on top.

Position

In Width: As given in the Directives/Standards mentioned in Section 28-1, Nos. 2 and 3.

In Height: The distance from the upper edge of the lamp's light emitting surface must not be more than 40 cm from the horizontal plane tangent to the upper, rearmost edge.

Alternative Standards: Lamps approved and marked according to the SAE or DOT Standard shall be accepted, provided that the colour is more or less in accordance with the Directives/Standards mentioned in Section 28-2, Nos. 2 and 3.

Art. 28-1, no. 4-15 shall read:

4.15. The Regulations in Section 28-1, Nos. 2 and 3, apply to stop lamps on vehicles and trailers, with the following additions:

Number of: 2 additional ones on top.

Position

In Width: As given in the Directives/Standards mentioned in Section 28-1, Nos. 2 and 3.

In Height: The distance from the upper edge of the lamp's light emitting surface must not be more than 40 cm from the horizontal plane tangent to the upper, rearmost edge

Alternative Standards: Lamps approved and marked according to the SAE or DOT Standard shall be accepted, provided that the colour is more or less in accordance with the Directives/Standards mentioned in Section 28-1, Nos. 2 and 3.

Art. 28-4, no. 12 shall read:

TAXI ROOF LAMPS

12. All taxis must have a faintly illuminated roof light which, when seen from the front and the rear, has the word "TAXI" and possibly also a licence number.

12.1 The glass cover of the lamp shall be of a material which emits a white light, and the license

number shall be black, minimum height 40 mm. The word "TAXI" may be integrated into the

Company's logo. The colour and the geometrical design of both "TAXI" and logo as

desired. The same applies to the size of the characters. The logo may cover up to 40% of the

area on which it is mounted.

12.2 The lamp must not be more than 400 mm long, 20 mm high, and 150 mm wide. The lamp shall be positioned externally on the roof of the vehicle, and symmetrically on the vehicles centre line in front of the rear edge of the front side door. The lamp must be so securely fixed to the vehicle that it cannot fall off. Magnetic fixing may be acceptable.

12.3. The lamp must be connected in such a way that it can be lit even when no other lamps on the vehicle are lit. It must meet the following requirements:

12.3.1 On taxis with a taximeter the lamp must be connected to the taximeter in such a way that it can only be illuminated when the taximeter is off.

12.3.2 On other taxis the lamp must be connected via a separate switch and connected to a tell-tale lamp easily visible from the driver's seat and indicates when the lamp is on.

II

The amendments come into force immediately.”