# Regulation on requirements for Automatic Catchweighers, annex 2, section 3

3.	Accuracy classes

  - The instruments are divided into primary categories designated b: 
X or Y 
as specified by the manufacturer.

  - These primary categories are further divided into four accuracy classes:
XI, XII, XIII and XIV
and
Y(I), Y(II), Y(a) and Y(b)
which shall be specified by the manufacturer.

  - The following accuracy classes shall be used for the following types of weighing:

XI	To be used where there is a need for very high accuracy.

XII	To be used where there is a need for high accuracy.

XIII	To be used for weighing of processed products and similar trade 
	transactions. 

XIV	To be considered by Justervesenet in each individual case.

Y(I)	To be used where there is a need for very high accuracy.

Y(II)	To be used where there is a need for high accuracy.

Y(a)	To be used for weighing of processed products and similar trade 
	transactions. Examples are marking scales / price marking scales. 

Y(b)	To be used  for calculation of freight, tariff, etc. In addition they may be used 	for weighing of sand, gravel, ore, garbage and goods of similar price 	categories, for example scales for weighing garbage trucks and wheel loaders.