# Regulation on requirements for Rail Weighbridges, annex 2, section 3 and 4

- Accuracy classes

  - Instruments are divided into four accuracy classes as follows:
	0,2, 0,5, 1 and 2.

  - The following accuracy classes shall be used for the following types of weighing:
	Class 0,2:		To be used for gods in trade transactions
	Class 0,5:		To be used for gods in trade transactions
	Class 1:		To be used for calculation of freight, tariff etc
	Class 2:		To be used for calculation of freight, tariff etc

4.	Maximum permissible error

4.1	The maximum permissible errors for weighing-in-motion of a single wagon or a total train are shown in table 1.

| Table 1 |
| --- |
| Accuracy class | Maximum permissible measurement error |
|  | At sale and re-verification of the instrument | During use of the instrument |
| 0,2 | ± 0.1 % | ± 0.2 % |
| 0,5 | ± 0.25 % | ± 0.5 % |
| 1 | ± 0.5 % | ± 1.0 % |
| 2 | ± 1.0 % | ± 2.0 % |

  - The maximum permissible errors for the weight of coupled or uncoupled wagons weighing-in-motion shall be one of the following values, whichever is the greatest:
- the value calculated according to Table 1, rounded to the nearest scale interval,
- the value calculated according to Table 1, rounded to the nearest scale interval for a weight equal to 35 % of the maximum wagon weight (as inscribed on the descriptive markings),
- one scale interval (d).

  - The maximum permissible errors of train weighing-in-motion shall be one of the following values, whichever is the greatest:

- the value calculated according to Table 1, rounded to the nearest scale interval,
- the value calculated according to Table 1, for the weight of a single wagon equal to 35 % of the maximum wagon weight (as inscribed on the descriptive markings) multiplied by the number of reference wagons (not exceeding 10) in the train, and rounded to the nearest scale interval,
- one scale interval (d) for each wagon in the train, but not exceeding 10 d.

4.4	When weighing coupled wagons, the errors of not more than 10 % of the weighing results taken from one or more passes of the train may exceed the appropriate maximum permissible error given in paragraph 4.2, but shall not exceed twice the maximum permissible error